SECTION 09650

RESILIENT FLOORING AND VINYL BASE

1.  	GENERAL:

1.1 	REFERENCES:  Drawings and general provisions of Contract, including General Conditions and Division 1 specifications, apply to work in this section.

1.2 	DESCRIPTION OF WORK

A.	SCOPE:  The extent of work shall be as shown on Drawings and called for in these 			Specifications.  Performance shall meet the requirements of these Specifications.  The 		work covered by this section of Specifications consists of the following:

B.	Extent of Vinyl Composition Tile Flooring and Vinyl Base as shown on the drawings.

1.3 	SUBMITTALS

A.	Submittals under this Section shall include:

1. 	Manufacturers' data and installation instructions on all specified products;

2.    	Color range;

3.  	Samples of vinyl composition tile flooring and vinyl base

4.  	Shop drawings indicating materials, pattern number, tile number, and manufacturer.

2.  	PRODUCTS:

  - VINYL COMPOSITION TILE:  Shall be “ Mannington Brushworks 1/8” gauge.  Checker Board Pattern, Color 710 Naples Blue in Bathrooms.  701 Titanium White & 700 Cerulean Mist Check Board.

  - Uniclic Select Cherry Laminate.

2.2 	SUBSTITUTIONS:  The contractor may substitute resilient flooring specified by manufacturer’s name with a product manufactured by a different company only with approval of Architect.  The substituted product shall be of equal quality and price range.

  - VINYL BASE MOLDING – shall be Johnsonite Cover Base 4”, 1/8 gauge.  Submit color for Architect’s approval.  See Architectural Drawings for locations.

  - ADHESIVES: shall be as recommended by the manufacturer.

3.  	EXECUTION:

3.1  INSTALLATION shall be done by skilled craftsmen using the adhesives recommended by the manufacturer and in accordance with the manufacturer's instructions.  The flooring contractor shall examine the subfloors and report all defects which have to be corrected before the application of flooring starts.  Concrete floors shall be smooth, free of any grooves and depressions, and brushed clean of any foreign matter.  Install all resilient flooring with joints tight, floor true, level and even with no bubbles, pops or other visible defects.  Cut to and around all permanent fixtures keeping vinyl tight to fixtures.  Vinyl also shall be installed under fixtures such as baseboard heating, and glued tight.  Wrap vinyl base around exterior corners.

3.2 	DURING WORK PROGRESS, remove all excess materials, extraneous mastic, and debris resulting from operations, which may disrupt the work of other trades.  The Contractor shall be responsible for keeping the floors clean, unstained and undamaged until the final completion of the building.

END OF SECTION