SECTION 09680

CARPET

1. 	GENERAL

1.1	REFERENCES:  	Drawings and general provisions of Contract, including General Conditions and Division 1 specifications, apply to work in this section.

  - DESCRIPTION OF WORK:

- Installation of “Roberts Strips” for carpeting.

- Installation of Carpeting as shown on plans or noted in these Specifications.

1.3	QUALITY ASSURANCE

A.	Finished installation shall comply with fire test specified in applicable Building Code.

B.	Architect/Engineer shall review first finished space for workmanship.  Accepted space shall 		serve as project standard.

C.	All carpets will meet UM44D

1.4 	SUBMITTALS

A.	Submittals under this Section shall include:

1.	Manufacturer's specifications and installation instructions on all specified products.

2. 	Samples:  one piece, 18" x 18", of each color and type of carpet provided.

B.	Deliver to Owner, neatly packaged and labeled, all usable carpet scraps over 2 sq. ft. or 8 in. 		in least dimensions: 1 percent of each type and color of carpet provided, in 12 ft. wide rolls; 		and 1 percent of each type of edge strip provided, in standard lengths.

C.  	Provide written maintenance program.

2. 	PRODUCTS

2.1 	CARPET shall be as follows:

- Units: Queen/Willow Run; Pad: Crestfoam Crushguard 7/16:” FHA approved.

Sutton SUV By Shaw: Bedrooms 93700 Wheat Field. Livingrooms to be 93501 Dove Tail.

B. 	Corridors: Mannington/Neotech Color Paramount (PAMO) style “Fantail”.

- Stairs: Rambler 26 oz. direct glue Color Thunderstorm 00113.

2.2 	CARPET must carry stamp confirming conformance to above and submitted to Architect 	for approval.

2.3	All Carpet areas to receive vinyl base, see drawings & section 09650.

3.  	EXECUTION:

3.1 	JOB CONDITIONS:

A.	Examine Subfloor for dampness, loose material, excessive irregularity, oily or waxy areas 	impeding adhesion, or other conditions which would prevent proper installation.  Verify that 	no incompatible curing compound has been used on newly-poured concrete.  	Commencement of work constitutes acceptance of subfloor.

B. 	Allow newly-poured concrete to cure as long as possible before installation of carpet, a 	minimum of 7 days, 28 days preferable.  Perform bond and moisture tests in accordance 	with carpet manufacturer's instructions, to verify that concrete is sufficiently cured, dried 	and then sealed.

C.	Broom-clean or vacuum surfaces to receive carpet, before beginning installation.  Apply 	primer-sealer to plywood or concrete sub-floor, if recommended by carpet or adhesive 	manufacturer.

D. 	Before proceeding with complete installation of carpet, install a representative sample area 		of each type of carpet provided over each type of substrate, to test for compatibility of 			adhesive to substrate at glue-down installation, and verify general appearance of finished 			installation.  If sample is securely bonded after 72 hours, final installation may proceed.

3.2  	INSTALLATION

A. 	Install carpet by direct glue-down unless noted otherwise.  Install Entry carpet in accordance 	with the manufacturer's recommendations.

B. 	Field measure each space to receive carpet.  Do not scale drawings.  Before beginning 			installation, verify that floor telephone and electrical outlets have been installed.

C.	At glue-down installations, apply manufacturer's recommended adhesive in accordance with 		manufacturer's instructions, observing proper safety precautions.  Apply adhesive in a 				uniform film with a steel trowel and proper size notches for correct coverage.  Avoid 				applying excess quantities so that adhesive bleeds through joints.  Apply adhesive only in 			area which dries or films over.  Avoid soiling adjacent walls and floors with adhesive.  			Promptly remove any spillage.  Broom or roll carpet to remove air bubbles and insure bond.

D. 	Install carpet wall to wall unless noted otherwise.  Fit carpet neatly into breaks, recesses, 			closets and alcoves, against bases, around pipes and penetrations, under saddles and 				thresholds, and around permanent cabinets and equipment.  Install Schluter metal strip 			wherever carpet edge does not abut vertical surface, of appropriate configuration to provide 		smooth transition to adjacent material.  Allowable variation from level for finished 				installation: 1/4 in. from level in any direction when tested with 10 ft. straight-edge.

E. 	Seams shall be flat, free from puckering, without twists, free from frayed edges.  Coat edges 		with seam adhesive at glue-down installation, hot-melt tape at cushion, and as recommended 		by manufacturer.  Patterns at seams shall match exactly.  Cut raw edges on a slight angle 			with surface yarns extending outward over backing material so that surface yarns mingle 			neatly at seams.

F. 	Seams shall be in accordance with approved seaming shop drawings and samples.  No seams 		will be accepted perpendicular to openings such as doors, stairs, and entries.  Seams at doors 		shall be centered directly under doors.  Seam at corridor change of direction shall follow 			inner wall line across corridor.

G.	Provide removable cut-out pieces over flush equipment requiring access such as telephone 		and power outlets.  Cut-outs shall be neatly edged and securely held in place with double-			edged tape all around.

H. 	Remove adhesive spots from carpet immediately with solvent.  Trim loose pieces of face 			yarn with sharp scissors.  Upon completion of installation, remove rubbish, 	selvages, 			wrapping paper, small scraps, etc., and vacuum with commercial-type vacuum cleaner.  			Remove soiling, by shampoo if necessary.  Cover finished work with kraft paper or 				polyethylene until Substantial Completion.

I. 	At completion of job, remove protective paper, vacuum or shampoo again if required.

END OF SECTION