SECTION 10800

TOILET AND BATH ACCESSORIES

1.  	GENERAL

1.1	REFERENCES:  Drawings and general provisions of Contract, including General Conditions and Division 1 specifications, apply to work in this section.

1.2	DESCRIPTION OF WORK:  The extent of work shall be as shown on Drawings and called for in these Specifications. The work under this section of Specifications includes furnishing and installing the items listed as indicated on Drawings.

2. 	PRODUCTS:

2.1 	TOWEL BARS AND TOILET PAPER HOLDERS:  shall be Nutone Hallmack “Coronado” series, size as shown on Drawings.

2.2 	SOAP DISH:  shall be equal to NuTone HM-621, or be integral with sink.

2.3 	DOUBLE HOOK FOR BATHROOM DOOR:  shall be equal to NuTone HM-682.

2.4 	SHOWER CURTAIN ROD: bath shall be equal to NuTone HM-382.  Curtains are not included.

  - GRAB BARS: Stainless steel, 1 ¼ " diameter, concealed mounting with snap flange, satin finish; Bobrick B-5806 Series, lengths as shown on drawings.

  - ALL APARTMENT UNITS: Surface Mounted Medicine Cabinet: Vienna 155130, 30 x 26

x 5½, with lights by NuTone, #SB23129, provide light bulbs.

2.7  NOTE:  Blocking for all accessories and grab bars must be provided.   See Section 06100 - Rough Carpentry.

2.8	NOTE:  The contractor shall submit shop drawings on every item specified in this section.  There shall be no substitutions without a written explanation from the subcontractor that the specified item is equal with the item specified by the architect.  All substitutions shall be approved by the Architect and the Owner.

3.  	EXECUTION:

3.1  All work shall be done by experienced craftsmen in first-class manner and high-grade finish.

  - All installations shall be in accordance with layout shown on plans and in strict conformity with the manufacturer's recommendations and secured into blocking or other framing with screws of adequate length and size to properly support accessories.  Grab bars must be able to sustain a 300# direct load pulling down or out on it.

END OF SECTION