SECTION 11450

RESIDENTIAL EQUIPMENT AND KITCHENS

1. 	GENERAL:

1.1	REFERENCES

A.	Drawings and general provisions on Contract, including General Conditions and 				Division 1 specifications, apply to work in this section.

B. 	Rough Carpentry:  Section 06100

C. 	Finish Carpentry:  Section 06200

D. 	Gypsum Drywall:  Section 09250

1.2 	DESCRIPTION OF WORK

A. 	The extent of work shall be as shown on Drawings and called for in these 					Specifications.  The work under this section of Specifications includes furnishing and 		installing the following items as indicated on Drawings.

B. 	Kitchen Cabinets - wall hung and base and countertops according to layout on drawings.

C.	Bathroom Vanities and Countertops

D. 	Refrigerator

E.  	Kitchen Ranges and Range Hoods

F. 	Plastic Laminate on wall adjacent to range

1.3 	SUBMITTALS

A. 	Submit manufacturer's product data and installation recommendations for all specified 		products.

B. 	Architect reserves the right to require samples of all products to be submitted.  				Acceptable samples will be returned and may be used in the work.

C. 	Submittals for countertops shall be in accordance with Section 06200, Finish Carpentry.

2.  	PRODUCTS

2.1	Kitchen Cabinets:

A. 	Shall be of wood construction, with wood finished reverse beveled doors, self closing 			hinges, adjustable shelves, dual tracks for drawers with nylon guides.

B.  	Cabinets to be Extreem Series by Armstrong.  Countertops to be postform plastic laminate. Cabinet front panels to be Cornet Series by Armstrong.

2.2 	Bathroom Vanities:  shall be equal to “Oasis Marble Tops” with built in bowl available through FW Webb Co.  (207) 784-4575. Coordinate with plumber for drilling holes to receive faucet.  Kitchen counter tops to be rounded edge preformed plastic laminate color by Architect.

2.3	Unit Refrigerator shall be Kenmore Model #46-60752, Energy Star, frost free, refrigerator-freezer, 17 cu. ft.

2.4 	Unit Kitchen Range to be; Kenmore Model #22-96012, white, self clean, radiant.  Handicap units Kitchen Range to be Frigidaire Model # FES300DS, slide in, up front controls, white, self clean, coil.

2.5	Unit Kitchen Range Hoods: to be microwave hood combination Kenmore Model #22-62612, ventless, white.

2.6 Unit Dishwasher to be Kenmore Energy Star Model #22-15142, white.

3. 	EXECUTION:

3.1	INSTALLATION

A. 	All installation shall be done in a quality first-class manner according to Drawings and 		layouts shown, and shall be according to manufacturer's recommendations.

B. 	Kitchen cabinets and vanities:   shall be installed by experienced cabinet installers in a 			craftsmanlike manner, as though this were really "cabinets".  Securely screw  cabinets to 		blocking in the walls.  Blocking shall be in place at top and bottom of wall and base 			cabinets (see Rough Carpentry Sec. 06100), and screws shall be long enough to 				penetrate blocking 1-1/4" minimum.  Cabinets shall be level and plumb.  If leveling 			cabinets puts them visually out of line with other elements (wall line, window sill, door 		casing, etc.) Architect shall be notified.  Countertops shall be tight to the wall and joints 		caulked.  Cabinets shall be tight to each other and in line.  All doors and drawers to 			open freely.  Work shall be left clean and right.

C. 	Refrigerators and ranges:  Shall be set in place properly hooked up and leveled.

D. 	Range hoods shall be new secured in place by means of screws hidden from view.

E. 	The contractor shall check and make necessary adjustments to insure that all installed 			items operate faultlessly.

F.	Touch up any dings, scratches or other marks with color matching original.

G. 	Contractor to coordinate installation of items in this Section with that of related 				mechanical trades:  15000 Plumbing and HVAC; 16000 Electrical.

H. 	All work under this SECTION shall be guaranteed to the Owner IN WRITING for a 			period of at least one (1) year.  Appliance Warranty and Operation Manuals to be 			provided to Owner with typed listing of appliance # correlated to Apt. #.

END OF SECTION