| Transportation Land Development Environmental S e r v i c e s |
| --- |
|  | 101 Walnut Street P. O. Box 9151 Watertown, MA 02471-9151 617 924 1770 FAX 617 924 2286 |
| Memorandum | To: | Sarah Hopkins Development Review Services Manager Department of Planning and Development City of Portland 389 Congress Street Portland, Maine 04101 | Date: | February 17, 2006 |
| Project No.: | 07334.00 |
|  | From: | John M. Hession | Re: | Morrill's Crossing – Waiver Request |

Sarah,

As part of the Morrill’s Crossing application, the applicant, Morrill’s Crossing, LLC, is requesting two waivers from the City of Portland, Maine Technical and Design Standards and Guidelines.

The first waiver request is from:

SECTION III – TRAFFIC DESIGN STANDARDS AND GUIDELINES

3.         STANDARDS: Parking Lot/Parking Space Design

A.         Parking space: The standard parking space is 9 feet wide by 19 feet long.

The applicant is requesting the use of parking spaces that are 9 feet wide by 18 feet long. Stop & Shop, the anchor tenant, operates over 300 stores and has found that, by using double white stripes and a 24 foot wide drive aisle, the 9 foot by 18 foot parking stall is sufficient. The reduction of one foot in the length of the parking stall reduces the overall impervious area of the development and allows for the inclusion of the longitudinal island in the main parking field and additional buffering in the vicinity of the townhomes.

The second waiver request is from:

SECTION XV – SITE LIGHTING STANDARDS

4.         SPECIFIC STANDARDS

A.         Uniformity

As Measured in foot candles at grade, maximum to minimum illumination levels shall not exceed a ratio of twenty (20) to one (1).

B.                  Illumination Levels

Minimum, Maximum, and Average illumination levels for areas intended to be lighted, as measured at grade, shall be:

Minimum:          0.2 foot candles

Maximum          5.0 foot candles

Average:           1.25 foot candles

The applicant is requesting to utilize ornamental (shepard’s hook style) lighting in three areas of the site; the main entrance drive, the townhome drive and the apartment parking lot. These ornamental fixtures are part of the urban streetscape design and are intended to provide visual interest as you enter the site and to differentiate the residential areas on the site from the commercial areas.  The photometrics for the ornamental fixtures with a 12 foot pole height and a 250 watt fixture result in maximum illumination level of 9.0 foot candles measured at grade directly below the fixture. These illumination levels drop off quickly as you get away from the fixture. Because the maximum illumination level of 9.0 foot candles exceeds the 5.0 foot candles allowed, we also exceed the twenty (20) to one (1) maximum to minimum ratio. The statistical area summary is shown on drawing SL-1, Site Lighting and Photometrics Plan.

You will note that the areas identified as Stop & Shop and Retail meet the standards. You will also note that the area identified as Boxing does not meet the minimum (0.0 foot candles verses 0.2 foot candles minimum required). We will address this area by providing additional lighting (to bring the minimum to 0.2 foot candles) and no waiver is requested.