# Packard Final Review: TRAFFIC

Traffic/Loading/Parking Standards

Site Plan, Conditional Rezoning, Subdivision, Traffic Movement Permit

## Site Plan Standards

- The provisions for vehicular loading and unloading and parking and for vehicular and pedestrian circulation on the site and onto adjacent public streets and ways; and the incremental volume of traffic will not create or aggravate any significant hazard to safety at or to and including intersections in any direction where traffic could be expected to be impacted; and will not cause traffic congestion on any street which reduces the level of service below Level "D" as described in the 1985 Highway Capacity Manual published by the Transportation Research Board of the National Research Council, a copy of which manual is on file with the pubic works authority, or substantially increase congestion on any street which is already at a level of service below Level "D";

(2)	a.	Where construction is proposed of new structures having a total floor area in excess of ten thousand (10,000) square feet but less than fifty thousand (50,000) square feet, or building additions having a total floor area in excess of five thousand (5,000) square feet, and the provisions for off-street parking under article III (zoning) do not require off-street parking or are determined to be insufficient, the site plan shall provide sufficient parking to satisfy the reasonably foreseeable demand for parking which will be generated by the proposed development;

- Where construction is proposed of new structures having a total floor area in excess of fifty thousand (50,000) square feet, the planning board shall establish the parking requirement for such structures. The parking requirement shall be determined based upon a parking analysis submitted by the applicant, which shall be reviewed by the city traffic engineer, and upon the recommendation of the city traffic engineer.

  - The proposed development is designed so as to be consistent with off-premises infrastructure, existing or planned by the city;

# Subdivision Ordinance

Sec. 14-497. General requirements.

(pertaining to townhouse condos, apartments over retail and rear apartments)

- Will not cause unreasonable highway or public road congestion or unsafe conditions with respect to use of the highway or public roads existing or proposed;

# Conditional Rezoning Standards

d.	Traffic improvements: PACKARD shall be responsible for the design and installation of, at minimum, the off-site traffic improvements shown on Exhibit C, which improvements shall be made at PACKARD'S sole expense, following review and approval by the CITY.  Such traffic improvements may include, but not be limited to, roadway widening, signal modifications, installation of a new traffic signal, provisions for bicycle facilities, bus stops, esplanades with street trees, railroad preemption upgrades and pedestrian facilities (e.g. sidewalks, crosswalks).  In addition, within twelve (12) months after issuance of the final certificate of occupancy for Phase I, PACKARD shall undertake a post-development traffic study of the unsignalized intersections identified within the scope of the MDOT traffic movement permit. In the event that this study demonstrates that the impact from traffic attributable to the development is materially different than what was approved as part of the project's MDOT traffic movement permit, the CITY may require PACKARD to fund mitigation measures to address those impacts, to the extent that such mitigation is technically and economically feasible.  As well, the applicant shall be obligated to mitigate impacts created by the development, to the extent technically and economically feasible, which result in a degradation of traffic service at said intersections.