March 25, 2009

Memo To:	Eric Giles

From: 		David Margolis-Pineo and Staff at Public Services

Re:		Morrill’s Crossing Review Comments

- Please note that the grease trap detail does not meet City standards.  Please contact Steve Harris at 874-8843.

- Existing Detail was shown on 2006 Site Plan

- Site drainage is headed for Washington Ave.  Has an evaluation been completed to verify the capacity of the culvert at Washington Ave.

  - Is not related to identifying changes from the 2006 Site Plan to the 2009 Site Plan.

- It has been reported that there are beaver in the area behind the Me DEP.  This should be verified and if so the beaver should be trapped and relocated.

  - Is not related to identifying changes from the 2006 Site Plan to the 2009 Site Plan.

- Capacity letter completed 4/29/05.  Have conditions changed to require a revised capacity letter?

- No

- There needs to be street lights on Morrill St.

- No street lighting was shown on 2006 Site Plan

- There should be 10" of gravel on sheet C-11 if sidewalk is in the City ROW.

- Sidewalk dimensions within the ROW have not changed from 2006 Site Plan

- Concrete is not allowed in the City ROW to backfill curbing.

- Concrete backfill was shown on 2006 Site Plan

- 3' sumps are the City standard in catch basins, not 4'.  But 4’ is permitted.

- Ok

- City standard is 6" of 3/4" crushed stone under all structures.

- 12” gravel is shown on 2006 Site Plan

- Catch basin frames and covers to be Ethridge E24" x 5” or approved equal is the City standard.

- Pre-Construction Meeting issue

- Pipe boots are required in all catchbasins pipe connections.

- Detail is not shown in 2006 Site Plan

- Inverts in DMH's are to be brick with concrete or masonry fill.

- Concrete is shown in 2006 Site Plan

- All pipes in the City right of way to be SDR 35 or RCP pipe, no HDPE is allowed.

- Sheet C1 shows installation of Sewer PVC and Storm Drain RCP

- The City standard for pipe installation is 6"under and 12" over of 3/4" crushed stone.

- Pre-Construction Meeting issue

- All storm drain manhole covers to be stamped DRAIN and all sanitary sewer manhole covers to be stamped SEWER.

- Ok

- No inside drops are allowed in a sanitary sewer manhole in the City ROW.

- None proposed

- All joints between sections of precast concrete structures to be double sealed with Butyl rubber.

- Details of 2006 Site Plan show the joints to be Preformed Butyl

- Curb installation to be per City standard.

- Curb installation is compliant with standard

- All work in the City ROW shall adhere to the Street Opening Rules and Regulations and preformed by a licensed excavator with the City of Portland.

- Pre-Construction issue

- The work in Allen Ave and Forest Ave is restricted to between 9 AM and 3:30 PM. A time waiver may be requested to work outside those hours from Public Services.

- Pre-Construction issue