SECTION 02201 – EARTHWORK - STRUCTURES

PART 1 - GENERAL

1.01 SUMMARY

A.	Perform excavation, filling, compacting and grading operations both inside and outside building limits as required for below-grade improvements and to achieve contours and elevations indicated.

B.	Provide subbase materials, drainage fill, and common fill materials for slabs, pavements, and improvements.

C.	Provide suitable fill from offsite if on-site quantities are insufficient, and dispose of excess fill offsite.

D.	Provide rock excavation without blasting unless blasting is specifically authorized.

E.	See also separate section for earthwork requirements at site areas.

1.02	SUBMITTALS

A.	Submit for approval test reports.

1.03	QUALITY ASSURANCE

A.	Comply with governing codes and regulations. Provide products of acceptable manufacturers which have been in satisfactory use in similar service for three years. Use experienced installers. Deliver, handle, and store materials in accordance with manufacturer's instructions.

PART 2 - PRODUCTS

2.01 MATERIALS

A. Subbase material: Gravel or crushed stone graded for intended use as subbase for paving materials specified.

B.	Drainage fill: Washed gravel or crushed stone, 1/4" to 3/4" size; ASTM C33, Size 67.

C.	Common fill: Mineral soil substantially free from organic and unsuitable materials, and free from rock or gravel larger than 2" in diameter; 80 percent passing No. 40 sieve and not more than 50 percent passing No. 200 sieve.

D.	Structural Fill: Gravel or sandy gravel free of organic and unsuitable materials and within the following gradation limits: 4" sieve, 100 percent finer by weight; 1" sieve, 60 to 100 percent; No. 4 sieve, 25 to 85 percent; No.20 sieve, 10 to 60 percent; No. 50 sieve, 4 to 35 percent; No. 200 sieve, 0 to 5 percent.

PART 3 - EXECUTION

3.01	INSTALLATION

A.	Excavation is unclassified and includes excavation to subgrade regardless of materials encountered. Repair excavations beyond elevations and dimensions indicated as follows:

1.	At structure: Concrete or structural fill.

2.	Elsewhere: Backfill and compact as directed.

B.	Do not perform any additional work without written authorization from the Owner if subgrade material is unsuitable for intended use.

C.	Maintain stability of excavations; provide shoring and bracing as required by authorities having jurisdiction. Prevent surface and subsurface water from accumulating in excavations. Stockpile satisfactory materials for reuse, allow for proper drainage and do not stockpile materials within drip line of trees to remain.

D.	Compact materials at the optimum moisture content as determined by ASTM D1557 by aeration or wetting to the following percentages of maximum dry density:

1.	Structure, pavement, walkways: Sudgrade and each fill layer to 95% of maximum dry density.

2.	Unpaved Areas: Top 6" of subgrade and each fill layer to 90% maximum dry density.

E.	Place acceptable materials in layers not more than 8" loose depth for materials compacted by heavy equipment and not more than 4" loose depth for materials compacted by hand equipment to subgrades indicated as follows:

1.	Structural Fill: Use under foundations, slabs on grade in layers as indicated.

2.	Drainage fill: Use under building slabs, at foundation drainage and elsewhere as indicated.

3.	Common Fill: Use under unpaved areas.

4.	Subbase Material: Use under pavement, walks, steps, piping and conduit.

F.	Grade to within 1/2" above or below required subgrade and within a tolerance of 1/2" in ten feet.

G.	Protect newly graded areas from traffic and erosion. Recompact and regrade settled, disturbed and damaged areas as necessary to restore quality, appearance, and condition of work.

H.	Control erosion and windblown dust. Dispose of waste and unsuitable materials off site in a legal manner.

END OF SECTION 02201