SECTION 06400 - ARCHITECTURAL WOODWORK

PART 1 GENERAL

1.01	SUMMARY

A.	Section Includes:

1.	Standing and Running Trim.

2.	Casework.

3.	Countertops.

4.	Wood Handrails.

5.	Closet Pole and Shelf.

B.	Related Sections:

1.	06100, Rough Carpentry.

2.	09900, Painting.

1.02	QUALITY ASSURANCE

A. 	Design Criteria:

1.	Reference Standards:

a.	Refer to AWI Quality Standards for definition of Premium, Custom, or Economy.

b.	Any item not given specific quality grade shall be Custom Grade.

1.03	SUBMITTALS

A. 	Shop Drawings:

1. 	Submit shop drawings showing detail construction of woodwork, based on Drawings, and modified or revised as may be required to achieve intended structural character.

2. 	Elevations: Draw at scale of min. 1/2 in. = 1 ft.

3.	Details: Draw at scale of min. 3 in. = 1 ft.

PART 2 PRODUCTS

2.01	MATERIALS

A.	Solid Lumber Stock:

1.	General: Comply with AWI 100, plain sawn, S4S and work to shapes indicated, unless otherwise indicated.

2.	Preservative Treatment - Exterior Woodwork: Refer to Section 06100, Rough Carpentry.

B.	Plywood:

1. 	Comply with AWI 200, veneer core.

2.	Face Veneer:

a.	Softwood: Douglas fir.

3.	Cut: Plain sliced, smooth.

C.	Particleboard:

1.	Comply with AWI 200 and CS236, mat formed.

2.	Density: NPA Grade 1-M-3.

3.	Finish:

a.	Paint or varnish all surfaces and edges not covered with plastic laminate.

b.	At cutouts made for particleboard countertops, seal all edges to prevent water damage or swelling of material.

D.	Hardboard:

1.	Comply with AWI 200, Grade 1, tempered smooth two sides for both side exposure, smooth one side for one side concealed.

2.	1/4 in. thick tempered for use as substitute for 1/4 in. plywood when surfaces are painted.

E.	Plastic Laminate:

1.	NEMA LD3 General Purpose Type 0.05 in. thick, finish and color as selected.

2.	Backing sheets on shelves 0.02 in. thick.

F.	Fasteners:

1.	Wood Screws: ANSI B18, type, size, and material as required for condition of use.

2.	Bolts and Nuts: ANSI B18 and ASTM A307 type, size, and material as required.

G.	Adhesives: Melanine, phenol-resin, or seasoned-resin to AWI standards and manufacturer's recommendations suited for purpose.

2.02	FABRICATION

A.	Standing and Running Trim and Rails:

1.	General:

a.	Quality Standard: AWI Section 300.

b.	Rout or groove backs of flat trim members, kerf backs of other wide flat members, except for members with ends exposed in finished work.

c.	Assemble casings in plant except where limitations of access to place of installation require field assembly.

2.	Exterior Trim - Opaque Finish:

a.	Grade: Custom.

b.	Lumber Species: Pine.

3.	Interior Trim - Opaque Finish:

a.	Grade: Custom.

b.	Lumber Species: Poplar

B.	Architectural Cabinets - Laminate Clad:

1.	Quality Standard: AWI Section 400 and Division 400B.

2.	Laminate Clad Cabinets:

a.	Grade: Custom.

b.	Type of Cabinet Construction: Flush overlay.

c.	Laminate Cladding: High pressure decorative

laminate complying with NEMA LD 3.

d.	Colors, Pattern and Finishes: As selected by Architect from laminate manufacturer's standard products.

3.	Laminate Grade - Exposed Surfaces:

a.	Horizontal Surfaces Other Than Tops: GP-50, 0.050 in. nominal thickness.

b.	Postformed Surfaces: PF-42, 0.042 in. nominal thickness.

c.	Vertical Surfaces: GP-50, 0.050 in. nominal thickness.

d.	Edges: GP-50, 0.050 in. nominal thickness.

e.	Semi-Exposed Surfaces: High pressure laminate, GP-28.

f.	Dust Panels: 1/4 in. plywood or tempered hardboard above compartments and drawers except where located directly under tops.

C.	Cabinet Hardware and Accessory Materials:

1.	Hardware Finishes:

a.	Comply with BHMA 1301 for finishes indicated by BHMA Code Numbers.

b.	626, satin chromium plated, brass or bronze base.

c.	652, satin chromium plated, steel base,

d.	630, satin stainless steel.

e.	Concealed Hardware: Provide manufacturer's standard finish complying with product class requirements of ANSI/BHMA A156.9.

2.	Hinges:

a.	Concealed, self-closing, 180 deg. operation.

b.	Product: Stanley Model 1503-2.

3.	Drawer Slides:

a.	Full extension, side mount, stay-close, self closing.

b.	Capacity: 100 lb.

c.	Manufacturer: Knape & Vogt, Grant Hardware Co.

4.	Pulls: Wire pulls, US3 bright brass clear coated finish, with 4” centers, or as selected.

5.	Locks:

a.	3/4 in. dia. disc tumbler, pivoting cam type with 1 in. throw.

b. 	Doors: 7/8 in. dia. disc tumbler, plunger type with 15/32 in. throw.

6.	Adjustable Shelf Hardware:

a.	Standards: 0.080 in. thick, 1/2 in. slots, 1 in. o.c., 11/16 in. wide.

b.	Bracket: 1-13/16 in. wide with reinforced top hook length as required.

D.	Countertops and Vanities:

1.	AWI 400C, Custom Grade for quality of fabrication.

2.	Finish: Plastic laminate.

3.	Core: NPA Grade 1-M-3 particleboard,

4.	Thickness: As detailed.

E.	Wood Handrails - Transparent Finish to match existing:

1.	Pressure glued and doweled end returns, eased edges to profiles indicated.

2.	Species: Poplar, utilize only lumber in which the light colored wood is presented on the front.  Dark or green colored wood can only be exposed on the side facing the wall.

3.	Provide radius finger grip on back edge of rail.

4.	Include all fillers, plugs, and mitered returns to match railing.

5.	Match existing, tie into existing where indicated.

F.	Closet Pole and Shelf:

1.	Shelf: 3/4 in. birch plywood with solid wood edgeboard stock, unless indicated otherwise.

2.	Pole:

a.	1-1/16" o.d. tubing.

b.	Product: Knape & Vogt Model 660 with 734 heavy duty flanges.

G.	Fasteners and Anchors:

1.	Screws:

a.	Select material, type, site, and finish required for each use.  Provide finish screws where nails cannot be used.

2.	Nails:

a.	Select material, type, size, and finish required for each use.

3.	Anchors:

a.	Select material, type, size, and finish required by each substrate for secure anchorage.

PART 3 EXECUTION

3.01	PREPARATION

A.	Examine substrates and adjoining construction, and conditions under which work will be installed.

B.	Do not proceed with work until conditions detrimental to proper and timely completion of Work have been corrected.

3.02	INSTALLATION

A.	General:

1.	Verify dimensions before proceeding and obtain measurements at site for Work required to be accurately fitted to other construction.

2.	Coordinate Work with other trades affected by this installation.

3.	Give particular attention to work of supporting and attachment items so as not to delay progress.

4.	Backprime lumber for painted finish exposed on exterior, or in moisture or humidity locations on interior, to requirements of Section 09900, Painting.

5. Discard material which is unsound, warped, bowed, twisted, improperly treated, too small to fabricate work with minimum joints, or of defective fabrication with respect to surface, size, or pattern.

6.	Scribe and cut work to fit adjoining work and refinish cut surfaces.

B.	Standing and Running Trim:

1.	Install with minimum joints using full-length pieces.

2.	Stagger joints in adjacent and related members.

3.	Cope at returns and miter at corners.

4.	Use scarf joints for end-to-end joints.

5.	Secure to grounds, stripping, and blocking with concealed and blind nails using fine finishing nails or finish screws.

C.	Casework:

1.	Install without distortion for proper opening and accurate alignment of doors and drawers.

2.	Adjust hardware to center doors and drawers.

3.	Anchor tops to base units and other support systems.

D.	Finishes: Refer to Section 09900, Painting, for field finished items.

3.03	FIELD QUALITY CONTROL

A.	Tolerances:

1.	Plumb and Level: 1/8 in. in 8 ft.

2.	Offset in Surface Alignment: Max. 1/16 in.

3.	Offset in Revealed Adjoining Surface: Max. 1/8 in

3.04	ADJUSTING AND CLEANING

A.	Adjustments:

1.	Repair damaged Work or replace with new to eliminate defects.

2.	Adjust joinery for uniform appearance.

3.	Clean, lubricate, and adjust hardware.

B.	Cleaning:

1.	Clean all surfaces.

2.	Provide protection and maintain installed condition until Substantial Completion

END OF SECTION 06400