SECTION 07240 - EXTERIOR INSULATION AND FINISH SYSTEM

PART 1 - GENERAL

1.01	SUMMARY

A.	Provide exterior insulation and finish system, with colors and shapes as indicated.

1.02	SUBMITTALS

A.	Submit for approval samples, shop drawings, product data, mock-ups, warranty.

1.03	QUALITY ASSURANCE

A.	Comply with governing codes and regulations. Provide products of acceptable manufacturers which have been in satisfactory use in similar service for three years. Use experienced installers. Deliver, handle, and store materials in accordance with manufacturer's instructions.

PART 2 - PRODUCTS

2.01	MATERIALS

A.	Portland cement topcoat over extruded polystyrene, mechanically attached, EIMA Class PM; Insul-Crete or approved equal.

B.	Acrylic polymer topcoat over expanded polystyrene, adhesively attached, EIMA Class PB; Dryvit or approved equal.

C.	Acrylic polymer topcoat over expanded polystyrene, mechanically attached; Sto Industries or approved equal.

PART 3 - EXECUTION

3.01	INSTALLATION

A.	Inspect substrate and report unsatisfactory conditions in writing; beginning work means acceptance of substrate.

B.	Comply with system manufacturer's instructions and recommendations; admixtures shall not be used. Provide reinforced base and finish coats to provide a uniform appearance. Completely cover all insulation board including edges. Trimbeads are not permitted unless approved. Provide soft joints at all changes of substrate and at intervals suggested by manufacturers and at approved locations. Install areas of special patterns where indicated on drawings. Clean and protect work.

END OF SECTION 07240