***** Paragraph Numbered Format ***** ******* Copyright 1988, ARCOM ******* ARCHITECTURAL COMPUTER SERVICES, INC.

SECTION 07600 - FLASHING AND SHEET METAL

THIS SECTION USES THE TERM "ARCHITECT." CHANGE THIS TERM AS NECESSARY TO MATCH THE ACTUAL TERM USED TO IDENTIFY DESIGN PROFESSIONAL AS DEFINED IN THE GENERAL AND SUPPLEMENTARY CONDITIONS.

PART 1 - GENERAL

1.1	SUMMARY

EDIT EXAMPLES BELOW BY DELETING ITEMS NOT REQUIRED, ADDING OTHERS, OR REVISING TEXT TO CLARIFY DESCRIPTIONS.

A.	This Section includes the following:

1.	Metal counter flashing and base flashing.

2.	Scuppers and downspouts (rain drainage).

3.	Exposed metal trim.

4.	Miscellaneous sheet metal accessories.

1.2	SUBMITTALS

A.	General:  Submit the following in accordance with Conditions of Contract and Division 1 Specification Sections.

B.	Product data, Flashing, Sheet Metal, and Accessories:  Manufacturer's technical product data, installation instructions and general recommendations for each specified sheet material and fabricated product.

RETAIN ABOVE AND INSERT SPECIFIC DATA SUBMITTALS AS DESIRED.

C.	Samples of the following flashing, sheet metal, and accessory items:

1.	8-inch-square samples of specified sheet materials to be exposed as finished surfaces.

DELETE ABOVE AND BELOW IF NO CONTROL REQUIRED ON SHEET MATERIALS.  DELETE BELOW IF VISUAL CONTROL OF TRIM UNITS, GUTTERS, DOWNSPOUTS, EXPANSION JOINT UNITS, ETC. IS NOT DESIRED.

2.	12-inch-long samples of factory-fabricated products exposed as finished work.  Provide complete with specified factory finish.

DELETE BELOW IF NONE OF WORK SUFFICIENTLY COMPLEX TO JUSTIFY SHOP DRAWINGS; EDIT TO DELETE NONAPPLICABLE UNITS.  POSSIBLY INSERT PRODUCT-HANDLING ARTICLE WHERE SUBSTANTIAL VOLUME OF HIGHLY FINISHED WORK IS REQUIRED.

D.	Provide mock-ups showing layout, profiles, methods of joining, and anchorages details, including major counterflashings, trim/fascia units, downspouts, scuppers, and expansion joint systems.

POSSIBLY INSERT QUALITY ASSURANCE ARTICLE HERE FOR LIMITATIONS ON FABRICATORS OR INSTALLERS OF COMPLEX SYSTEMS OF FLASHING, RAIN DRAINAGE, EXPANSION JOINTS, ETC.

POSSIBLY INSERT HERE SPECIAL PROJECT WARRANTY REQUIREMENTS FOR EXTENSIVE/ ELABORATE (ESPECIALLY PREFAB) SYSTEMS.

PART 2 - PRODUCTS

2.1	SHEET METAL FLASHING AND TRIM MATERIALS

REVISE BELOW IF BRIGHT OR POLISHED FINISH REQUIRED (FOR TRIM), OR IF TERNE-COATED DESIRED (DARK GREY, PAINTABLE).

A.	Provide typically unless indicated otherwise: Copper:  ASTM B 370; temper H00 (cold-rolled) except where temper 060 is required for forming; 16 oz. (0.0216-inch thick) except as otherwise indicated.

REVISE ABOVE (AND BELOW) AS DESIRED, INCLUDING FINISH PREPARED FOR PAINTING, OR "ALCLAD" SHEET, ETC.  INSERT OTHER SHEET METALS AS REQUIRED, INCLUDING ZINC ALLOY, TERNE COATED SHEET, WEATHERING STEEL, ETC.

B.	Provide where indicated: Sheet Aluminum:  ASTM B 209, alloy 3003, temper H14, AA-C12C42R1X baked enamel finish; 0.040-inch thick (20 gauge) except as otherwise indicated. Color selected by architect.

REVISE ABOVE IF MILL FINISH FOR PAINTING, COLOR ANODIZED, OR ACRYLIC FINISH DESIRED.

ABOVE PERFORMANCE REQUIREMENTS ARE "LENIENT", BUT RULE OUT SOME VINYL SHEETS BECAUSE OF LOW-TEMP. BRITTLENESS (REVISE TO MINUS 20 DEG F FOR INCLUSION). REINFORCED SHEETS DEFEAT PURPOSE OF THIS TYPE SHEET IN ITS PRIME USE.  USUALLY RETAIN ONE OR MORE OF FOLLOWING GENERIC CHOICES, OR INSERT LISTING OF ACCEPTABLE PRODUCTS/ MANUFACTURERS; SEE EVALUATIONS.

BELOW IS ONLY ONE EXAMPLE OF MANY AVAILABLE COMPOSITION FLASHING MATERIALS FOR NONEXPOSED USE.  SOLID-SHEET AND REINFORCED FLEXIBLE PVC CAN BE USED FOR SOME OF SAME APPLICATIONS.

2.2	LAMINATED COMPOSITION SHEET FLASHING

A.	Copper/Paper Flashing:  5-oz. copper sheet laminated between 2 sheets of bituminous impregnated creped Kraft paper or saturated fabric.

B.	Available Products:  Subject to compliance with requirements, products that may be incorporated in the Work include, but are not limited to, the following:

RETAIN ABOVE FOR NONPROPRIETARY OR BELOW FOR SEMIPROPRIETARY SPECIFICATION.  REFER TO DIVISION 1 SECTION "MATERIAL AND EQUIPMENT."

1.	Afco Products, Inc.; "Cop-A-Bond Duplex."

2.	Phoenix Building Products, Inc.; "Duplex Cop-R Flash."

3.	York Manufacturing, Inc.; "Cop-R-Tex Duplex."

D.	Miscellaneous Materials and Accessories:

E.	Solder:  For use with steel or copper, provide 50 - 50 tin/lead solder (ASTM B 32), with rosin flux.

G.	Fasteners:  Same metal as flashing/sheet metal or other non- corrosive metal as recommended by sheet manufacturer.  Match finish of exposed heads with material being fastened.

H.	Bituminous Coating:  SSPC - Paint 12, solvent-type bituminous mastic, nominally free of sulfur, compounded for 15-mil dry film thickness per coat.

I.	Mastic Sealant:  Polyisobutylene; nonhardening, nonskinning, non- drying, nonmigrating sealant.

POSSIBLY INSERT SPECIFIC PERFORMANCE REQUIREMENTS BELOW OR ACCEPTABLE PRODUCT LISTING FOR CRUCIAL APPLICATIONS OF SEALANTS.  (COORDINATE WITH DIV 7 SECTION "JOINT SEALERS.")

J.	Elastomeric Sealant:  Generic type recommended by manufacturer of metal and fabricator of components being sealed and complying with requirements for joint sealants as specified in Division 7 Section "Joint Sealers."

K.	Epoxy Seam Sealer:  2-part noncorrosive metal seam cementing compound, recommended by metal manufacturer for exterior/interior nonmoving joints including riveted joints.

L.	Adhesives:  Type recommended by flashing sheet manufacturer for waterproof/weather-resistant seaming and adhesive application of flashing sheet.

M.	Paper Slip Sheet:  5-lb. rosin-sized building paper.

N.	Polyethylene Underlayment:  Minimum 6-mil carbonated polyethylene film resistant to decay when tested in accordance with ASTM E 154.

O.	Reglets:  Metal or plastic units of type and profile indicated, compatible with flashing indicated, noncorrosive.

P.	Metal Accessories:  Provide sheet metal clips, straps, anchoring devices, and similar accessory units as required for installation of work, matching or compatible with material being installed, noncorrosive, size and gage required for performance.

Q.	Conductor-Head Guards:  20-gage bronze or nonmagnetic stainless steel mesh or fabricated units, with selvaged edges and noncorrosive fasteners.  Select materials for compatibility with downspouts.

R.	Elastic Flashing Filler:  Closed-cell polyethylene or other soft closed-cell material recommended by elastic flashing manufacturer as filler under flashing loops to ensure movement with minimum stress on flashing sheet.

S.	Roofing Cement:  ASTM D 2822, asphaltic.

INSERT OTHER MATERIALS AS REQUIRED FOR PROJECT.

2.4	FABRICATED UNITS

A.	General Metal Fabrication:  Shop-fabricate work to greatest extent possible.  Comply with details shown and with applicable requirements of SMACNA "Architectural Sheet Metal Manual" and other recognized industry practices.  Fabricate for waterproof and weather-resistant performance, with expansion provisions for running work, sufficient to permanently prevent leakage, damage, or deterioration of the work.  Form work to fit substrates.  Comply with material manufacturer instructions and recommendations for forming material.  Form exposed sheet metal work without excessive oil-canning, buckling, and tool marks, true to line and levels indicated, with exposed edges folded back to form hems.

B.	Seams:  Fabricate nonmoving seams in sheet metal with flat-lock seams.  For metal other than aluminum, tin edges to be seamed, form seams, and solder.  Form aluminum seams with epoxy seam sealer; rivet joints for additional strength where required.

C.	Expansion Provisions:  Where lapped or bayonet-type expansion provisions in work cannot be used or would not be sufficiently water/weatherproof, form expansion joints of intermeshing hooked flanges, not less than 1 inch deep, filled with mastic sealant (concealed within joints).

D.	Sealant Joints:  Where movable, nonexpansion type joints are indicated or required for proper performance of work, form metal to provide for proper installation of elastomeric sealant, in compliance with SMACNA standards.

INSERT SPECIFIC LISTING (BELOW) OF SEPARATIONS KNOWN TO BE REQUIRED FOR WORK AS DETAILED.  ATTEMPT SHOULD BE MADE (IN DETAILING AND SELECTING MATERIALS) TO AVOID THIS NEED.

E.	Separations:  Provide for separation of metal from noncompatible metal or corrosive substrates by coating concealed surfaces at locations of contact, with bituminous coating or other permanent separation as recommended by manufacturer/fabricator.

F.	Aluminum Extrusion Units:  Fabricate extruded aluminum running units with formed or extruded aluminum joint covers for installation behind main members where possible.  Fabricate mitered and welded corner units.

DELETE PARAGRAPH BELOW IF NOT DESIRED (OR IF NO GUTTERS AND DOWNSPOUTS); OR REVISE TO ANOTHER TYPE FINISH OR COLOR.

REVISE PROVISIONS OF ARTICLE BELOW AS DESIRED (AND AVAILABLE).  REPLACE TYPES BELOW WITH SIMILAR PROVISIONS FOR AN ALUMINUM EXTRUSION SYSTEM WHERE DESIRED, SUCH AS OFFERED BY CONSTRUCTION SPECIALTIES, HICKMAN OR MM SYSTEMS.  OTHER PROPRIETARY SYSTEMS WHICH INCLUDE SUBSTANTIAL CURB CONSTRUCTIONS AS PART OF UNIT SHOULD BE SPECIFIED IN SECTION "ROOF SPECIALTIES AND ACCESSORIES."

PART 3 - EXECUTION

3.1	INSTALLATION REQUIREMENTS

A.	General:  Except as otherwise indicated, comply with manufacturer's installation instructions and recommendations and with SMACNA "Architectural Sheet Metal Manual." Anchor units of work securely in place by methods indicated, providing for thermal expansion of metal units; conceal fasteners where possible, and set units true to line and level as indicated.  Install work with laps, joints, and seams that will be permanently watertight and weatherproof.

B.	Underlayment:  Where stainless steel or aluminum is to be installed directly on cementitious or wood substrates, install a slip sheet of red rosin paper and a course of polyethylene underlayment.

C.	Bed flanges of work in a thick coat of bituminous roofing cement where required for waterproof performance.

D.	Install reglets to receive counterflashing in manner and by methods indicated.  Where shown in concrete, furnish reglets to trades of concrete work for installation as work of Division 3 sections.  Where shown in masonry, furnish reglets to trades of masonry work, for installation as work of Division 4 sections.

DELETE ABOVE IF NO REGLETS REQUIRED.  ADJUST PROVISIONS OF TEXT TO CONFORM WITH LOCAL PRACTICE AND TRADE JURISDICTIONS.

E.	Install counterflashing in reglets, either by snap-in seal arrangement or by welding in place for anchorage and filling reglet with mastic or elastomeric sealant, as indicated and depending on degree of sealant exposure.

G.	Install "beehive"-type strainer-guard at conductor heads, removable for cleaning downspouts.

INSERT OTHER SPECIFIC INSTALLATION REQUIREMENTS FOR OTHER SYSTEMS AND SHEET METAL ACCESSORY ITEMS SPECIFIED AS WORK OF THIS SECTION.

3.2	CLEANING AND PROTECTION

A.	Clean exposed metal surfaces, removing substances that might cause corrosion of metal or deterioration of finishes.

B.	Protection:  Advise Contractor of required procedures for surveillance and protection of flashings and sheet metal work during construction to ensure that work will be without damage or deterioration other than natural weathering at time of Substantial Completion.

END OF SECTION 07600