SECTION 07820 - METAL FRAMED SKYLIGHTS

PART 1 - GENERAL

1.01	SUMMARY

A.	Provide metal framed, insulating glass skylights.

1.02	SUBMITTALS

A.	Submit for approval: samples, shop drawings, product data, mock-up, warranty.

1.03	QUALITY ASSURANCE

A. Comply with governing codes and regulations. Provide products of acceptable manufacturers which have been in satisfactory use in similar service for three years. Use experienced installers. Deliver, handle, and store materials in accordance with manufacturer's instructions.

PART 2 - PRODUCTS

2.01	MATERIALS

A.	Pre-engineered glass and metal frame assemblies designed for loading conditions and exposure: Extruded aluminum with Kynar 500 finish and 1 3/16” laminated insulating glass units; Wasco Pinnacle 300, or approved equal products by Naturalite Vistawall or Supersky. Provide Solarban 60 low-E coating on glazing.

PART 3 - EXECUTION

3.01	INSTALLATION

A.	Comply with manufacturer's recommendations and instructions. Coordinate installation with roofing system to ensure weathertight performance.

B.	Isolate dissimilar metals and metals from treated wood.

C.	Provide and install all flashings and counterflashings needed to provide a weathertight assembly.

D.	Restore damaged components and finishes. Clean inside and outside surfaces prior to project substantial completion and protect work from damage.

END OF SECTION 07820