***** Paragraph Numbered Format ***** ******* Copyright 1988, ARCOM ******* ARCHITECTURAL COMPUTER SERVICES, INC.

SECTION 08305 - ACCESS DOORS

PART 1 - GENERAL

1.1	SUMMARY

A.	This Section includes access doors for installation in the following types of construction:

REVISE BELOW TO SUIT PROJECT.

1.	Gypsum drywall or veneer plaster.

B.	Provide fire-rated access doors where indicated or scheduled, or in fire-rated assemblies.

REVISE BELOW TO SUIT PROJECT.

1.2	SUBMITTALS

A.	General:  Submit the following in accordance with Conditions of Contract and Division 1 Specification Sections.

1.	Product data in form of manufacturer's technical data and installation instructions for each type of access door assembly, including setting drawings, templates, instructions, and directions for installation of anchorage, devices.

a.	Include complete schedule, including types, general locations, sizes, wall and ceiling construction details, finishes, latching or locking provisions, and other data pertinent to installation.

DELETE ABOVE AND BELOW IF NO CUSTOMIZED UNITS REQUIRED.

PART 2 - PRODUCTS

2.1	MANUFACTURERS

A.	Available Manufacturers:  Subject to compliance with requirements, manufacturers offering access doors that may be incorporated in the work include, but are not limited to, the following:

RETAIN ABOVE FOR NONPROPRIETARY OR BELOW FOR SEMIPROPRIETARY SPECIFICATION. REFER TO DIVISION 1 SECTION "MATERIALS AND EQUIPMENT."

1.	Bar-Co., Inc.

2.	Cesco Products

3.	J.L. Industries

4.	Karp Associates, Inc.

5.	Milcor, Inc.

6.	Nystrom, Inc.

7.	The Williams Brothers Corp.

MOST MFRS CAN PROVIDE ALL ACCESS DOORS LISTED IN SECTION; NYSTROM MAKES ONLY FIRE-RATED FLUSH PANEL UNITS.

2.2	MATERIALS AND FABRICATION

A.	General:  Furnish each access door assembly manufactured as an integral unit, complete with all parts, and ready for installation.

B.	Steel Access Doors and Frames:  Fabricate units of continuous welded steel construction unless otherwise indicated.  Grind welds smooth and flush with adjacent surfaces.  Furnish attachment devices and fasteners of type required to secure access panels to types of support shown.

C.	Frames:  Fabricate from 16-gage steel.

ABOVE IS STANDARD FOR LISTED MANUFACTURERS. NORMALLY RETAIN ABOVE AND DELETE BELOW UNLESS STAINLESS STEEL PANEL REQUIRED.

1.	Fabricate frame with exposed flange nominal 1-inch wide around perimeter of frame for units installed in the following construction:

a.	Exposed masonry.

b.	Exposed concrete.

c.	Drywall finish.

d.	Ceramic tile finish.

e.	Wood paneling.

RETAIN APPLICABLE CONSTRUCTIONS ABOVE AND BELOW. INSERT OTHERS THAT REQUIRE AN EXPOSED FLANGE TRIM OR SPECIALTY.

2.	For gypsum drywall or gypsum veneer plaster, furnish perforated frames with drywall bead.

3.	For installation in masonry construction, furnish frames with adjustable metal masonry anchors.

RETAIN BELOW FOR NORMAL INSTALLATIONS.

E.	Flush Panel Doors:  Fabricate from not less than 14-gage sheet steel, with concealed spring hinges or concealed continuous piano hinge set to open 175 degrees.  Finish with manufacturer's factory-applied prime paint.

NORMALLY RETAIN ABOVE AND DELETE BELOW UNLESS STAINLESS STEEL FINISH REQUIRED. COORDINATE WITH FRAME MATERIALS.

IF EITHER OF ABOVE APPLIES, RETAIN BELOW FOR FIRE RATED UNITS; DELETE IF NONE REQUIRED. SELF-CLOSING MECHANISM NOT USUALLY PROVIDED ON UNITS LESS THAN 12 INCHES BY 12 INCHES.

1.	For fire-rated units, provide manufacturer's standard insulated flush panel/doors, with continuous piano hinge and self-closing mechanism.

1.	Furnish recessed panels for concealed installation in acoustic tile ceiling systems, and gypsum drywall ceilings of apartment units.

DELETE ABOVE OR BELOW; NEITHER OR BOTH.

RETAIN BELOW FOR ALL PANELS. NUMBER DEPENDS ON TYPE AND SIZE OF DOOR. CYLINDER LOCK (IF SPECIFIED) BELOW REPLACES ONE CAM LOCK.

F.	Locking Devices:  Furnish flush, screwdriver-operated cam locks of number required to hold door in flush, smooth plane when closed.

OTHER AVAILABLE LOCKING DEVICES INCLUDE: RING PULL, ALLEN HEAD, PHILLIPS HEAD, SPANNER HEAD, TEE HANDLE, PUSH BUTTON, AND THUMB TURN DEVICES. REVISE TEXT ABOVE IF SUCH DEVICES REQUIRED.

RETAIN BELOW IF ALL ACCESS DOORS REQUIRE CYLINDER LOCKS.

RETAIN BELOW IF LIMITED NUMBER OF ACCESS DOORS REQUIRE CYLINDER LOCKS. COORDINATE WITH HARDWARE SCHEDULE.

1.	Where shown or scheduled, provide one cylinder lock per access door.  Furnish 2 keys per lock.  Key all locks alike unless otherwise indicated.

DELETE BELOW IF NO RECESSED PANEL DOORS.

2.	For recessed panel doors, provide access sleeves for each locking device.  Furnish plastic grommets and install in holes cut through finish.

PART 3 - EXECUTION

3.1	INSTALLATION

A.	Comply with manufacturer's instructions for installation of access doors.

B.	Coordinate installation with work of other trades.

DELETE BELOW IF NO FRAMES WITH MASONRY ANCHORS REQUIRED.

C.	Set frames accurately in position and securely attach to supports with face panels plumb or level in relation to adjacent finish surfaces.

3.2	ADJUST AND CLEAN

A.	Adjust hardware and panels after installation for proper operation.

B.	Remove and replace panels or frames that are warped, bowed, or otherwise damaged.

POSSIBLY ADD "ACCESS DOOR SCHEDULE."

END OF SECTION 08305