SECTION 08520 - ALUMINUM WINDOWS

PART 1 GENERAL

1.01	SUMMARY

A.	Section Includes:

1.	Window Unit.

2.	Glazing.

3.	Screens.

1.02	QUALITY ASSURANCE

A.	Reference Standards: ANSI/AAMA A101.85; comply with applicable requirements except as otherwise indicated.

B.	Design Criteria:

1.	Performance Requirements: Fabricate units to comply with requirements and performances to match existing.

a.	Comply with High Performance requirements of ANSI A101.85, Sec. 3.

b.	Fabricate units with integral thermal barrier to provide 45 condensation resistance factor, AAMA 1502.6.

c.	Provide improved construction tolerances and weatherstripping to limit air infiltration to 0.10 cu. ft. per min. per ft. of crack at edge of operable sash; tested by ASTM E283, for 20 percent of pressure resulting from design wind loading.

1.03 	SUBMITTALS

A. 	Product Data:

1.	Submit product data, including half-size details of each typical section, showing glazing detail.

2.	Submit specific information on operating parts, hardware, weatherstripping, finishes for aluminum, and preglazed construction.

B.	Samples: Submit finish samples on 12 in. length of extrusions.

1.04	WARRANTY

A.	Special Project Warranty:

1.	Submit written warranty, signed by Manufacturer, Installer and Contractor, agreeing to replace aluminum window units which fail in materials or installations within 3 years of date of Acceptance.

2.	Failure of materials or installation shall include, but not be limited to, excessive leakage or air infiltration, excessive deflections, faulty operation of sash, deterioration of finish or metal in excess of normal weathering, and defects in hardware, weatherstripping, and other components of Work.

PART 2 PRODUCTS

2.01	MATERIALS

A.	Windows,hardware, screens, weatherstripping: match existing windows.

B.	Window Types - Operation:

1.	Fixed and double hung with muntins in the glass.

C.	Product: Traco (verify same manufacturer as existing). Provide low-E coating.

PART 3 EXECUTION

3.01	INSTALLATION

A.	General:

1.	Anchor window units securely in place, with permanent separations to prevent electrolytic corrosion.

2.	Seal entire perimeter of each unit as shown; comply with requirements of Section 07900, Joint Sealers.

3.	Adjust and lubricate operating sash and hardware for proper operation.

4.	Clean aluminum surfaces promptly after installation; do not damage protective coating; repair minor damage of finish.

5.	Clean glass promptly after installation.

6.	Operate each window to ensure engaging locking mechanism and leave window units in locked, closed position.

END OF SECTION 08520