SECTION 10950 - MISCELLANEOUS SPECIALTIES

PART 1 - GENERAL

1.01	SUMMARY

A.	Section Includes:

1. Fire Extinguishers and Fire Extinguisher Cabinets

2. Drapery Track hardware

3. Corner Guards

4. Mirror at Treatment Room

1.02	QUALITY ASSURANCE

A.	Source Quality Control:

1.	Field Measurements:

a.	Take field measurements before preparation of shop                         drawings and fabrication, where possible, to ensure proper fitting of Work.

b.	Allow for adjustments within specified tolerances                                                                                                                                    where taking of field measurements before fabrication might delay the Work.

B.	Coordination: Furnish inserts and anchorages which must be built into other Work for installation of related Work; coordinate delivery with other Work to avoid delay.

1.03	SUBMITTALS

A.	Product Data: Submit manufacturer’s detailed technical data for materials, fabrication, and installation, including catalog cuts of anchors, hardware, fastenings, and accessories.

B.	Shop Drawings: Submit shop drawings for fabrication and erection of assemblies not fully described by product drawings, templates, and instructions for installation of anchorage devices built into other Work.

C.	Samples:

1.	Submit full range of color samples for each type of unit required.

2.	Submit 6 in. square samples of each color and finish on same substrate to be used in Work, for color verification after selections have been made.

PART 2 PRODUCTS

2.01	MATERIALS

A.  Fire Extinguishers and Fire Extinguisher Cabinets:

1.	Provide fire extinguishers of types as indicated for each fire extinguisher cabinet (FEC) and other locations indicated. Type:

a.	Multi-Purpose Dry Chemical Type A (4A:80B:C) UL rated 4-A; 80-BC, 10-lb nom capacity,aluminum container, 20” high, Amerex Model #B456

2.	Provide fire extinguisher cabinets; manufacturer’s standard units of suitable size for housing fire extinguishers of type and capacity indicated, and as follows;

a.	Recessed: Cabinet box recessed in wall to suit trim style selected.

b.	Trimless with Hidden Flange: Frame of cabinet box overlaps surrounding wall finish, concealed from view by overlapping door.  J.L. Industries Model “Embassy”, #5614 V10 FX.

B.	Drapery Track Hardware: (At all windows).

1.	Traverse Rod: 0.0245 in. steel, telescoping, white finish.

2.	Curtain Carrier: Molded acetal resin rollers with swivel-action drapery carrier.

3.	Mounting: 0.060 in steel wall return bracket.

C. 	Corner Guards: (4'-0" high) See plan for locations.

1.	Cover: 0.110 in high impact vinyl-acrylic material. Impact resistant. ASTM D256, 350 psi. Color and finish: Matte, color as selected. Retainer: extruded aluminum.

2. 	Fasteners: Gypsum board, #8 x 1 in SMS.

3. 	Closure Caps: High impact nylon.

4. 	Product: Pawling Rubber Corp., CG-11R at end walls, CG-20R at 90 degree corners, and CG-135R at 135 degree corners.

D.	Mirror at Treatment room over lavatory: Bobrick 165-2430

PART 3 EXECUTION

3.01	INSPECTION

A.	Examine substrates and adjoining surfaces before installation to ensure adjacent Work has been completed.

3.02	INSTALLATION

A.	General:

1.	Install specialties to manufacturer’s recommendations.

2.	Do not install before completion of Work by other trades on adjacent surfaces.

3.	Coordinate requirements for cutouts and openings in wall for recessed mounted units in conjunction with Section 04200, Unit Masonry, or Section 09250, Gypsum Board.

B.	Fire Extinguisher Cabinets:

1. Comply with NFPA 10, securely fasten to structure, square and plumb, in accordance with manufacturer’s instructions.

3.03	ADJUSTING AND CLEANING

A.	Clean all surfaces at time of installation and before final acceptance by Owner.

B.	Repair all surfaces damaged during installation.

END OF SECTION 10950