DRAFT

PLANNING BOARD REPORT

PORTLAND, MAINE

Capisic Pond Enhancement

Capisic Street

Final Level III Site Plan

Project #:   2013-268    CBL 192-C001001

City of Portland, Doug Roncarati, Stormwater Program Coordinator, DPS, applicant

| Submitted to: Portland Planning Board Public Hearing Date: March 25th, 2014 | Prepared by: Jean Fraser, Planner Date: March 21st, 2014 |
| --- | --- |

- Introduction

Woodard & Curran have submitted a final Level III Site plan application on behalf of the City of Portland for an enhancement project to the Capisic Pond within the Capisic Pond Park on the north side of Capisic Street. The project was considered at a PB workshop on January 28, 2014.

The project involves the removal of cattails and sediments from historically open waters using mechanical excavation methods and then replanting with a diverse range of vegetation that will support a greater diversity of habitat and help maintain the open water area.  The area of disturbance is approximately 8 acres.

Overall the project is important to allow the pond to remain classified as a moderate value Inland Waterbird and Waterfowl Habitat by the Maine Department of Inland Fisheries and Wildlife. The project is located within the City’s Recreation Open Space Zone and Stream Protection Overlay Zone with a small part also within the Shoreland Overlay Zone.  The entire area is within the “AE” Flood Area.

The project has been revised in response to Workshop comments (Attachment N and revised Plans P2., P3., and P4.) with additional information on truck traffic, construction management, tree preservation and the NRPA Permit public meeting and application (Attachment O).

This hearing has been noticed to 354 local neighbors and interested citizens with a legal advertisement in the Portland Press Herald on March 10th and 11th, 2014.  A Neighborhood Meeting was held on January 21, 2014 (Certificate and Notes in Attachment M).  The Planning office has not received any public comments as of the time of preparing this Report.

Required reviews;

The project is being reviewed as a Level III Site Plan because the scale of the disturbance is over 3 acres and it includes park improvements over 20,000 sq ft .  It also requires NRPA, Army Corps and MDEP permits due to the impacts on significant Wildlife Habitat and wetlands and scale of disturbance to land (described in Attachment D).

Waiver requests:

The project does not necessitate any waivers but the applicant has requested a three year period of validity for the approval if granted (rather than 1 year with a later request for an extension of 2 years) because the funding for this anticipates a summer 2015 start on site.

- PROJECT DATA

| Area of site: | 784,080 sq ft (18 acres) |
| --- | --- |
| Proposed area of disturbance: | 357,300 sq ft (8.2 acres) |
| Impervious surfaces: | none |
| Zoning: | ROS; Shoreland; Stream Protection |
| Land Use: | Public park (Capisic Pond Park) |
| Estimated Cost of the Project: | $2,090,000 |

III.	BACKGROUND/EXISTING CONDITIONS

Capisic Pond is the City of Portland’s largest freshwater water body and the surrounding park is well used by area residents and bird watchers. The application (Project Description in Attachment B) explains it is a man made pond created by dams that were first installed in the 1600’s and recent weir modifications.

It is classified by the Maine Department of Inland Fisheries and Wildlife (MDIFW)  as a moderate-value Inland Wading Bird and Waterfowl habitat, which is considered “Significant Wildlife Habitat” under the State law.

The pond has become overgrown with invasive cattails which have reduced the open water area from about 7.7 acres (1950’s) to about 2 acres.  This problem has accelerated over the last 10 years and has developed into a cattail monoculture and dense cattail stands that reduce the water flow, the open water areas and the range of plant species -  all of which reduce its value as a wildlife habitat.

The project anticipates funding to be confirmed for a start in 2015 (summer) and all approvals are expected to be in place in the next few month so that final construction documents can be prepared by the end of 2014.

IV.	PROPOSED DEVELOPMENT

The proposals are described in detail in Attachment H and Attachment N;  it is illustrated in the Plans P1-P8 and the illustrative material in Plan P9.  In summary the project proposes to remove the cattails and sediment from the pond area and modify the pond edge profile, then replant with a range of suitable plant species as shown in this extract form the Plan P9 series of illustrations:

This will entail reduction in the water level to allow for mechanical excavation and dredging and removal of materials by truck.  The amount of material to be removed is substantial and will involve hundreds of truck loads.  The final Construction Plan (Plan P4) shows three proposed construction vehicle access locations on Capisic Street and associated protection measures.

V.	PUBLIC COMMENT AND WORKSHOP

The applicant has held a number of public meetings on this project since July 2011 and the proposals reflect neighbor input as well as discussions with State permitting agencies. The Planning Office has not received any written comments and the Planning Board did not raise any particular issues over and above those highlighted by staff  in the Workshop Memo.

VI.	RIGHT, TITLE AND INTEREST

The City (applicant) owns all of the pond area impacted by the project to the north of Capisic Street but the improvements and construction access will also be undertaken on areas of the Pond that are privately owned to the south of Capisic Street.  The Citys Legal Department is working with the Project Engineer to secure easements for these areas and a potential condition of approval requires these to be secured and recorded prior to the issuance of a building permit.

VII.	STAFF REVIEW

- ZONING ASSESSMENT

The applicant has submitted an assessment of zoning (Attachment F) and the Zoning Administrator has approved the project subject to conditions (Attachment 2):

This project is located in an ROS zone with floodplain and shoreland overlay.  Floodplain regulations [14-450.8(c)} state: "All development associated with altered or relocated portions of a watercourse shall be constructed and maintain in such a manner that no reduction occurs in the flood carrying capacity of the watercourse."  This project is to specifically open up the closed in areas by overproductive cat-o-nine tails. The pond is being brought back to a healthier state with this "clean-out".

Shoreland/Stream protection also allows clearing within the pond to historically open areas [14-14-449(e)3 & 4]. 14-449(d)  allows the excavation or similar activities, however that section of the Shoreland Zone goes on to list best management practices that must be met and within the time frames given in the Ordinance.  The applicant shall follow these required practices during the construction work.

Zoning approves the work being proposed.

- SITE PLAN STANDARDS

The project is unusual in that it does not involve building construction and many of the site plan standards are not applicable.  However, the project affects a large area and is surrounded by residential and institutional uses and the review below addresses the impacts of the project.

- Transportation

- Impact on surrounding street system

The project involves an intense period of sediment removal near the start of the contract and Tom Errico, Traffic Engineering reviewer, had requested further information on the truck traffic generation, sightlines and truck routes.  The applicant has provided this information in Attachment M.   Mr Errico has confirmed that the traffic levels are not expected to be problematic form a capacity or safety perspective and that the sight distances for the construction access points meet city standards (Attachment 3).

- Construction Management Plan

The written Construction Management Plan in Attachment K explains this aspect of the project in detail, and revised Plan P2, Notes 30, 31 and 32) clarify truck traffic routes and requirements for sweeping of the ROW. The issue of truck routes is a concern because the preferred route goes by the main drop off and pick up location for Breakwater School (grades pre-school to 8th) and Tom Errico has commented (Attachment 3):

A proposed truck routing plan shall be documented.  It is my understanding that it is likely that trucks will be destined to the City of Westbrook via Brighton Avenue.  Accordingly, it seems reasonable that the routing consist of travel along Capisic Street to Brighton Avenue. I would suggest that truck activity avoid peak drop-off and pick-up times at Breakwater School.  Also, provisions to ensure that vehicles are cleaned prior to entering the public street system should be included.

Status: The applicant has provided a routing program that I find acceptable.  This should be considered a 		condition of approval.

The following condition of approval, based on Tom Errico’s comments, is suggested:

That the applicant and contractors and all associated truck operators shall follow the submitted routing program and avoid the peak drop off and pick up times at Breakwater School, and that Breakwater School shall be formally advised, 3 weeks prior to the start of any associated truck traffic, of the times of truck traffic so that they may advise parents of the arrangements;   and

- Sidewalk and ROW

The Plan (Note 30 on Plan P2. And P4.) has  been revised to address the previous DPS comments that requested that the contractor be responsible for any sweeping due to materials inadvertently falling on the roadway between the dredge and disposal site.

{add DPS comments here}

(B)	Environmental Quality Standards

- Preservation of Significant Natural Features

The project team has been working with the MDEP, MDIFW, and the Army corps of Engineers to ensure that the impacts on the existing wildlife and habitats are fully understood and addressed. As confirmed in Attachment D, a NRPA Permit is required along with Army Corps and other MDEP permits and the application is included at Attachment O.  the application is currently under review and the applicant is addressing questions from the MDEP.  The applicant has requested, and staff recommend, that the receipt of NRPA and other required State permits be a condition of approval.

- Landscape Preservation

The City Arborist had previously highlighted the need for some “treesaves” in the vicinity of the construction access off the north side of Capisic Street.  The Existing Conditions Plan (Plan P3.) has been revised to identify the larger existing trees in the vicinity of the proposed construction access.  The Construction Plan (Plan P4) has shown these trees and confirmed that two are proposed for removal to allow for the construction access.

The City Arborist has confirmed these proposals are acceptable and anticipates being involved as the project progresses.

- Stormwater and Erosion control

The project does not result in any additional impervious area and therefore the only requirements under Chapter 500 and the City’s Technical standards relate to erosion and sedimentation control (see Attachment I). The Site Details Plan (P7) includes notes/details for the measures proposed to control erosion and sedimentation.

(C)	Public Infrastructure and Community Safety Standards

- Consistency with City Master Plans/infrastructure

The City has made a significant investment over the past 15 years in improving the Capisic Brook watershed through combined sewer overflow improvements and stormwater management, with additional steps identified in the Capisic Brook Watershed Management Plan adopted in November 2012. The proposed project complements the other initiatives as well as addressing other State and local objectives.

(D)	Site Design Standards

(these do not apply to this project)

VIII.	Staff Recommendation

The project is a large-scale and impacts a large neighborhood.  Although it is part of a wider project that began in 2011, the site plan process has provided an opportunity for the public and site plan reviewers to ensure that there are unlikely to be any concerns once the project commences.  Staff recommend that the approval be extended to three years (normally one year, with option to extend another 2 years if requested prior o the expiration of one year) and to the granting of approval subject to the receipt of NRPA and other permits since these are largely involved with technical details.

IX.   	MOTIONS FOR THE BOARD TO CONSIDER

- DEVELOPMENT REVIEW

On the basis of the application, plans, reports and other information submitted by the applicant, findings and recommendations contained in the Planning Board Report for the public hearing on March 25, 2014 for application #2013-268  Capisic Pond Enhancement,  relevant to the Site Plan reviews and other regulations, and the testimony presented at the Planning Board hearing, the Planning Board finds the following:

Site Plan Review

The Planning Board finds that the plan (is/is not) in conformance with the site plan standards of the Land Use Code, subject to the following condition(s) of approval:

Potential conditions of approval:

- That a copy of the NRPA, Army Corps and MDEP permits shall be submitted to the Planning Authority prior  to 	the issuance of a building permit.  If there are significant modifications to the proposals as a result of the these 	reviews, then an amended site plan would be required for approval by the Planning Authority prior to the 	issuance of a building permit; and

- That the applicant shall obtain easements or temporary construction agreements for all work outside the 	boundaries of the site, to be reviewed and approved by Corporation Counsel and the recorded copies shall be 	provided to the Planning Authority  prior to the issuance of a building permit; and

- That the applicant and contractors and all associated truck operators shall follow the submitted routing program 	(including Notes on Plan 2 G-001) and avoid the peak drop off and pick up times at Breakwater School, and 	that Breakwater School shall be formally advised, 3 weeks prior to the start of any associated truck traffic, of the 	times of truck traffic so that they may 	advise parents of the arrangements;  and

- That the best management practices and timeframes listed and required in the City of Portland Ordinances for the 	Shoreland Zone shall be followed during the construction work; and

- That this approval is valid for 3 years from the date of Planning Board approval.

ATTACHMENTS

Staff Review Comments

- City Arborist comments 3.20.2014 and 1.17.2014

- Zoning Administrator comments 1.22.2014

- Traffic Engineering Review comments 3.20.2014

- DPS Engineering comments 1.24.2014 and (update awaited)

Public Comments

(None received as of completion of this Report).

Applicants Submittal

- Application

- Project Description

- Right, Title and Interest

- Evidence of State and Federal Approvals

- Financial and Technical Capacity

- Zoning Assessment

- Conformance with Site Plan Standards

- Significant Natural Features

- Stormwater Management

- Solid Waste

- Construction Management Plan

- Fire Department Review

Received since Workshop:

- Public/Neighborhood Meeting Documents

- Response to Workshop comments 3.3.2014

- NRPA application

Plans

P1.	Cover sheet and Index

P2.	General Notes and legend (revised)

P3.	Existing conditions (revised to show trees)

P4.	Construction Plan (revised)
P5.	Landscaping Plan

P6.	Landscaping Details

P7.	Site Details

P8.	Site Details (revised)

P9.	Pond Cross sections and illustrations (12)