## Memorandum

Department of Planning and Urban Development

Planning Division

TO:		Stuart O’Brien, Chair and Members of the Portland Planning Board

FROM:	Jean Fraser,  Planner

DATE:		January 24, 2014

RE:		Capisic Pond Enhancement

Capisic Street

City of Portland (Doug Roncarati, DPS), applicant

Project #:   2013-268    CBL 192-C001001

MEETING DATE:   January 28, 2014

- Introduction

Woodard & Curran have submitted a Level III Site plan application on behalf of the City of Portland for an enhancement project to the Capisic Pond within the Capisic Pond Park on the north side of Capisic Street.

The project involves the removal of cattails and sediments from historically open waters using mechanical excavation methods and then replanting with a diverse range of vegetation that will support a greater diversity of habitat and help maintain the open water area.  The area of disturbance is approximately 8 acres.

Overall the project is important to allow the pond to remain classified as a moderate value Inland Waterbird and Waterfowl Habitat by the Maine Department of Inland Fisheries and Wildlife.

The application (Attachment X) describes the background to the project and  outlines how the project will enhance the aesthetic, recreational and education opportunities of the park as well as addressing the MDIF&W criteria.

The project is located within the City’s Recreation Open Space Zone and Stream Protection Overlay Zone with a small part also within the Shoreland Overlay Zone.  The entire area is within the “AE” Flood Area.

The project is being reviewed as a Level III Site Plan because the scale of the disturbance is over 3 acres and it includes park improvements over 20,000 sq ft .  It will also require permitting under NRPA, Army Corps and MDEP due to the impacts on significant Wildlife Habitat and wetlands and scale of disturbance to land.

- Project Data

| Area of site: | 784,080 sq ft (18 acres) |
| --- | --- |
| Proposed area of disturbance: | 357,300 sq ft (8.2 acres) |
| Impervious surfaces: | none |
| Zoning: | ROS; Shoreland; Stream Protection |
| Land Use: | Public park (Capisic Pond Park) |
| Estimated Cost of the Project: | $2,090,000 |

III.	Background/Existing conditions

Capisic Pond is the City of Portland’s largest freshwater water body and the surrounding park is well used by area residents and bird watchers. The application (Project Description) explains it is a man made pond created by dams that were first installed in the 1600’s and recent weir modifications.

The pond has become overgrown with invasive cattails which have reduced the open water are afrom about 7.7 acres (1950’s) to about 2 acres.  This problem has accelerated over the last 10 years and ow threatens the

III.	Proposed Development

Proposals

Construction

IV.	Staff Review

- Zoning Assessment

- Site Plan Standards

V.	Next Steps

PB Memo re Capisic Pond Improvement Project

ATTACHMENTS

Staff Review Comments

- City Arborist comments 1.17.2014

- Zoning Administrator comments 1.22.2014

- Traffic Engineering Review comments 1.23.2014

Public Comments

PC1.

Applicants Submittal  (all 12.16.2013)

- Application

- Project Description

- Right, Title and Interest

- Evidence of State and Feral Approvals

- Financial and Technical Capacity

- Zoning Assessment

- Conformance with Site Plan Standards

- Significant Natural Features

- Stormwater Management

- Solid Waste

- Construction Management Plan

- Fire Department Review

- Neighborhood Meeting Invitation

Plans

- Cover sheet and Index

- General Notes and legend

- Existing conditions

- Construction Plan

- Landscaping Plan

- Landscaping Details

- Site Details

- Site Details

- Pond Cross sections (3)