Plain text = ND ORIGINAL COMMENTS; ORANGE = ND 9/19; BROWN = ND 11/20

PURPLE = DMP ORIGINAL COMMENTS; BOLD = DMP 9/19

RED = DS ORIGINAL COMMENTS; ARIAL BOLD = DS 9/19

BLUE = ANN ORIGINAL COMMENTS; BLUE = ANN 9/26

14-403

- Transportation Standards

DMP:

A turnaround is required at the end of the proposed street, per the City of Portland Technical Manual and the Department of Public Services.  Please define with easements.   No turnaround added.  ADDED TURNAROUND

Sidewalk crossing details with ADA warning strip shall be reviewed and approved by Bruce Hyman (400-9243) of the Department of Public Services. No crossing detail is now shown.  ADDED DETAIL, BUT NOT CLEAR HOW SIDEWALK INTERFACE WORKS W/O CURBING.

DS:

- In accordance with Section 1 of the City of Portland Technical Manual:

  - The aggregate base course for a bituminous sidewalk should be 10” of Type B gravel per Figure I-12.

  - Vertical granite curbing and terminal curb details should be per Figure I-16.

As in 2005, the applicant has requested a sidewalk waiver for the west side of Pomeroy Street. This waiver was granted for the prior submittal. However, a new sidewalk waiver request, complete with justification, should be submitted as part of the current proposal. NOT PROVIDED.  PROVIDED AND OKAY.

- Environmental Quality Standards

DS:

  - The previous site plan prepared in 2005 was granted a MaineDEP Tier 1 NRPA Permit for 13,028 square-feet of wetland disturbance; the current amended project will disturb only 10,462 square-feet, and the applicant intends to work with MaineDEP to coordinate the update of this permit. Woodard & Curran recommends that the approved amended MaineDEP permit be forwarded to the Planning Division upon receipt.  The Applicant has stated that they intend to submit the updated MaineDEP Tier 1 NRPA Permit upon receipt.  NO PERMIT PROVIDED.  STATE WILL BE RESUBMITTED BASED ON REVISED NUMBERS AND PROVIDED AT LATER DATE.

  - The site plan proposes two drainage pipe inlets located on either side of the residential driveway. These inlets have proposed invert elevations that are below the existing ground surface elevation, and are located in close proximity to existing wetlands. Surface and shallow groundwater associated with these wetland areas will likely enter the roadway drainage system through these inlets, affecting the hydrology of the adjacent wetland areas. Although review of wetland impacts will be performed by MaineDEP, the addition of this “non-contaminated” water source into a drainage system that discharges into the city’s combined sewer is not allowed unless approved by the City Engineer (Section 2.1.1 of City of Portland Technical Manual). Refer to Comment 1 in memo from David Margolis-Pineo, Dept. of Public Services dated September 19, 2012.  ELIMINATED CURBING, ELIMINATED DRAINAGE PIPES, and ADDED CULVERT UNDER DRIVEWAY.  DRAINAGE EASEMENTS REQUIRED?

  - NEED CURB WAIVER.  PROVIDED AND OKAY.

- The project falls within the Capisic Brook Watershed, which is classified as an Urban Impaired Stream by the MaineDEP. The City of Portland requires that all development, except single and two-family homes, subject to City of Portland review, shall be required to comply with the Urban Impaired Stream Standard pursuant to MaineDEP Chapter 500 Stormwater Management Rules if they are located within an Urban Impaired Stream watershed (Technical Manual, Section 5. II. Applicability in Portland. A.). A project in the direct watershed of an urban impaired stream must pay a compensation fee (as allowable by the City) or mitigate project impacts by treating, reducing, or eliminating an off-site or on-site pre-development impervious stormwater source following the guidance outlined in MaineDEP Chapter 500 standards. The Level II Site Plan application associated with the Pomeroy Street construction shall be subject to meeting the Urban Impaired Stream Standard. The application must address a means of meeting the Urban Impaired Stream Standard. The applicant requests to pay an In-Lieu Compensation Fee to meet the UIS Standard.  The Applicant should provide a calculation of the fee based on the table in MaineDEP Chapter 500 Section 6.A.(1); refer to Technical Manual, Section 5 for a copy of the Chapter 500 Standards.  PROVIDED CALCULATION FOR UNCLEAR AREA.  IMPERVIOUS CALCULATION DOES NOT REPRESENT WHOLE STREET.

- The City of Portland requires that all Level II site plan applications submit a stormwater management plan pursuant to the regulations of MaineDEP Chapter 500 Stormwater Management Rules, including the Basic, General, and Flooding Standards (Technical Manual, Section 5. II. Applicability in Portland. C. a. and City of Portland Code of Ordinances Sec. 14-526. Site plan standards. (b).3.b.):

  - Basic Standards: The plans and application for both the Pomeroy Street construction and the single family residential lot have been prepared in accordance with the Basic Standards.

  - General Standards: Based on the Project Data Sheet submitted by the applicant, the new roadway (Level II Site Plan Application) will create 7,731 SF of new impervious area and approximately 11,500 SF of “disturbed area.” The applicant must provide a stormwater management plan addressing the general standards for the new impervious and developed area, and the site plan must include stormwater best management practices in conformance with the general standards. Comment has not been addressed by the applicant.

  - Flooding Standard: The applicant has provided a Stormwater Management Report with a HydroCAD analysis of the 2, 10, and 25 year, 24 hour storm events modeled for the predevelopment and post-development conditions. The runoff analysis indicates that the project will reduce peak flowrates at the project study point, a combined sewer inlet on Bancroft Street. The applicant should address the following:

      - The input parameters for Sheet Flow for SA-1 (Pre) and SA-11 (Post) should be the same, as this area will not change as a result of the project. The time of concentration lines for SA-1 (Pre) and SA-11 (Post) are shown on Sheets 6 & 7.  These Tc lines show a 150’ length of SHEET flow at the far east edge of the drainage boundary.  Because there are no proposed changes in this area, the HydroCAD model should reflect the same slope and cover type for this 150’ length of sheet flow in the pre & post condition. Please revisit the model and adjust accordingly.

- The Stormwater Management Plan will need to include a stormwater inspection and maintenance plan for all stormwater BMP’s designed to meet the General Standards, developed in accordance with and in reference to MaineDEP Chapter 500 guidelines and Chapter 32 of the City of Portland Code of Ordinances. The Applicant has stated that they will add an Appendix D to The Stormwater Management Plan, which will include reference to Chapter 32 of the City of Portland Code of Ordinances. The revised Stormwater Management Plan has not been received at this time.   ADDED APPENDIX D W/ CHAPTER 32.

- Public Infrastructure and Community Safety Standards

DMP:

- The City of Portland Technical Manual (adopted 7/19/10 and revised 6/17/11) states in 2.1.1, “The introduction of non-contaminated water such as rain water, non-contact cooling water, groundwater from foundation drains, sump pumps, surface drains or any other sources of inflow shall not be allowed to discharge into a sewer which conveys sanitary waste unless approved by the City Engineer.  When no other practical alternatives exist, this condition may be waived by the City Engineer.”  If the City Engineer should allow what is being proposed, a hydraulic analysis should be conducted to assure there will not be backups to the city’s sewer due to the additional surface water drainage.  The applicant is encouraged to seek an alternative mechanism for managing stormwater.  The applicant has not changed the design.  The design as shown is not allowable.  SEE ABOVE RE CURBING & DRIVEWAY CULVERT.

- The proposed pipe into existing sanitary manhole does not meet Technical Manual standards. Design still does not meet Technical Manual Standards.  REVISED

- Drain manholes shall have channels installed.

- All precast structure castings shall meet Technical Manual requirements or approved equal.

- As shown, drainage easements may be required.  (Note that the Planning Division will review this comment and provide further information on any necessary easements.)

DS:

- Proposed storm drain piping within the city right-of-way (ROW) shall meet the material requirements noted in Section 2.5.2 of the City of Portland Technical Manual. The plans should note an acceptable storm drain pipe material or note acceptable pipe material options for storm drain pipe within the city ROW.

- In accordance with Section 2 of the City of Portland Technical Manual:

  - Precast Manholes should be per Figure II-1.

  - Precast Catch Basins should be per Figure II-2.

  - Typical Pipe Trenches should be per Figure II-12.

- Site Design Standards

DMP:

Street light spacing and type should meet Technical Manual requirements.  I am checking on the statement made in Note 21 stating that CMP will supply.  This assumption may change. Applicant will be required to supply and install all street lighting which will become the property of the City upon street acceptance.  Lighting shall meet City standards which includes installing a meter.  Please add a note to consult with Kevin Thomas 9233-4912) prior to installation.  NOTE ADDED.

Additional Submittals Required:

- Please add a note to plans that all work within the proposed Pomeroy Street right-of-way shall meet City of Portland Technical Manual standards.

- On Sheet 1 please indicate the status of the streets shown (i.e. accepted, vacated, paper, etc).  In addition, please show Kenilworth Street.  A separate survey plan for acceptance is suggested.  KENILWORTH IS VACATED.  UPDATED NOTE.

- Please indicate the total right-of-way width and distances to property lines on Sheet 1.

- Sheet 1 should be on the Maine State Plane for acceptance.

- Sanitary manhole rims are not acceptable as an official city benchmark. The site bench mark is now on a PK in Bancroft St.  What City of Portland benchmark was used to set this benchmark (Note 22)?

- Please define the area of Pomeroy St. to be accepted with linework, bearings and distances and granite survey monuments. Bearings and distances are now shown but the information is not clear with all the over writes.  A clear separate roadway survey plan for acceptance will be required.  NOT PROVIDED.

- Please provide evidence of the applicant’s financial capacity to complete the proposed development.  PROVIDED LETTER SHOWING WINDSOR CONSTRUCTION HAS CAPACITY.  EMAIL FROM ANDY MORRELL 9/20 STATES THAT WINDSOR CONSTRUCTION WILL FINANCE THE PROJECT FOR THE APPLICANT.  PROVIDED LETTER FROM GORHAM SAVINGS STATING THAT KING WEINSTEIN HAS CAPACITY TO FINANCE WILANSKY PROJECT.

- Please submit plans for the attendant single family residence for purposes of clarification of uses.

SINGLE FAMILY

Environmental

- As noted in the city’s comments regarding your proposal for the construction of Pomeroy Street (dated 6/13/12), there are considerable wetlands and drainage issues on the site.  As designed, there is a significant possibility that the site’s wetlands will be drained into the city’s combined sewer system, ultimately changing the hydrology of the surrounding area.  The city’s Department of Public Services has indicated that non-contaminated water will not be allowed to discharge into the sewer system unless no other practical alternatives exist (see comments from David Margolis-Pineo, dated May 31, 2012 and David Senus, dated May 30, 2012, attached here).  Other outlets or mitigation measures should be explored.

- In accordance with Section 14.526(b)2.a., 30% of trees over 10” DBH within the setback should be preserved. ADDED NOTE.  CHECK W/ JEFF RE IDENTIFYING IN FIELD.  JT SAYS NOT NECESSARY.

- Two street trees are required per single family lot.  Please clarify whether additional trees will be planted or existing trees will be preserved in order to meet this requirement. PLACED ACROSS STREET.  IS THIS SUFFICIENT? JT SAYS OK.

Zoning

In addition, Ann Machado, the city’s zoning administrator , has requested:

- A written description of the outsale of the land that will be recorded at the registry of deeds. PROVIDED.  ANN 9/26 EMAIL “before certificate of occupancy can be issued, our office needs the recorded description of the out sale parcel.’

That the site plan show the footprints of the three porches that are shown on the building plans. Third, I still can't sign off on the site plan. Two of the three porches are now shown but the 8' x 47' porch on the "front" of the house, north side, facing Bancroft Street is not shown on the site plan.  ADDED PORCH?

Additional Submittals Required:

- Updated site plans to include:

  - Distances to property lines

  - Limit of disturbance

  - Foundation/perimeter drain outlet

  - Existing vegetation to be preserved

  - Proposed site landscaping

  - Accurate portrayal of building footprint (including porches) DOES NOT SHOW PORCHES. ADDED PORCH

- Updated NRPA Tier 1 permit.  WILL FORWARD UPON RECEIPT.  REVISED APPLICATION; WILL FORWARD LATER (INCLUDE AS CONDITION)

- Written description of existing easement on north side of property PROPOSED.  NOT PROVIDED.  BUT THIS IS OK.

- Information regarding site lighting.  As a reminder, exterior lighting should be full cut off.   SEE DMP’s COMMENT ON STREET LIGHTS

Note that review from the Fire Prevention Bureau is still pending.  The Planning Authority will forward comments from Fire Prevention as soon as they become available.  OKAY PER CP 7/11/12

- Applicant must meet waiver conditions to eliminate a sidewalk on one side of Pomeroy St.  PROVIDED.