Planning & Urban Development Department

Jeff Levine, Director

Planning Division

Alexander Jaegerman, Director

September 26, 2012

| Chabad Lubavitch of Maine, Inc. 101 Craigie Street Portland, ME 04102 | Andrew Morrell BH2M 28 State Street Gorham, ME 04038 |
| --- | --- |

RE:   Staff Review Comments for Single Family and Level II Site Plans

Project Name:	Pomeroy Street Single Family Home & Street Construction	Project ID:  2012-471

Applicant:	Chabad Lubavitch of Maine, Inc.				CBL:           193-E-1

Planner: 	Nell Donaldson

Dear Mr. Morrell:

Thank you for submitting a set of revised plans for both the construction of approximately 200’ of Pomeroy Street and the associated single family home.  The Planning Authority has evaluated the revised plans and found that a number of comments from the original review letters, dated 6/13/12 and 7/11/12, were fully addressed.  However, several of the city’s original comments and concerns remain.  They are as follows.

14-403 Street Extension, Additional Comments

- Transportation Standards

As originally noted by David Margolis-Pineo, of the city’s Department of Public Services:

- Per the City of Portland Technical Manual, a turnaround is required at the end of the proposed street.  The driveway cannot serve this function.  Please add a turnaround and define with easements.

- A crosswalk detail, including ADA warning strip, should be provided for review and approval by Bruce Hyman of the City’s Department of Public Services.

Although a sidewalk waiver request was granted for your 2005 submittal, a new sidewalk waiver request is required.  This waiver request should include justification for the waiver citing the waiver criteria from Section 14-506 of the city’s land use ordinance.

- Environmental Quality Standards

It has been noted that an updated MaineDEP Tier 1 NRPA permit will be forwarded upon your receipt.

The site plan continues to include drainage pipe inlets below the existing groundwater elevation.  It is likely that adjacent surface and groundwater will enter the roadway drainage system through these inlets, permanently affecting the hydrology of the area.  In addition, as proposed, the drainage system connects to a combined sewer line in Bancroft Street.  David Margolis-Pineo, of the city’s Department of Public Services, indicated in his original comments that an alternative mechanism for managing storm and groundwater should be found.  He also cited the city’s Technical Manual, stating that “when no other practical alternatives exist, this condition [the prohibition from discharging non-contaminated water into a sanitary sewer] may be waived by the city engineer.”  In your most recent submission, dated 8/29/12, you requested such a waiver.  However, it has not been shown that “no other practical alternatives exist,” and it should be noted that a waiver is highly unlikely.  The design should be altered so as to mitigate the drainage situation.

It should be noted that we understand that these plans are similar in nature to those of a prior project, approved in 2005.  However, there have been significant updates to both the city’s site plan ordinance and the Technical Manual since that time.  The current plans are being reviewed under the current ordinance.

Regarding the Urban Impaired Stream Standard, David Senus, the city’s consulting civil engineer, writes,

The applicant requests to pay an In-Lieu Compensation Fee to meet the UIS Standard.  The Applicant should provide a calculation of the fee based on the table in MaineDEP Chapter 500 Section 6.A.(1); refer to Technical Manual, Section 5 for a copy of the Chapter 500 Standards.

David Senus also notes that the comments regarding the General Standards of the state’s Chapter 500 Stormwater Management Rules have not been addressed.

Regarding your response to comments on the Flooding Standard, David Senus writes,

The time of concentration lines for SA-1 (Pre) and SA-11 (Post) are shown on Sheets 6 & 7.  These Tc lines show a 150’ length of SHEET flow at the far east edge of the drainage boundary.  Because there are no proposed changes in this area, the HydroCAD model should reflect the same slope and cover type for this 150’ length of sheet flow in the pre & post condition. Please revisit the model and adjust accordingly.

David Senus also notes,

The Applicant has stated that they will add an Appendix D to The Stormwater Management Plan, which will include reference to Chapter 32 of the City of Portland Code of Ordinances. The revised Stormwater Management Plan has not been received at this time.

- Public Infrastructure and Community Safety Standards

As originally noted by David Margolis-Pineo, the proposed pipe into existing sanitary manhole does not meet Technical Manual standards.

- Site Design Standards

Regarding street lights, David Margolis-Pineo, writes:

Applicant will be required to supply and install all street lighting which will become the property of the City upon street acceptance.  Lighting shall meet City standards which includes installing a meter.  Please add a note to consult with Kevin Thomas 9233-4912) prior to installation.

Additional Submittals Required:

- Please confirm that Kenilworth Street is a paper street.  Our records indicate that it has been vacated.

- David Margolis-Pineo writes,

The site benchmark is now on a PK in Bancroft St.  What City of Portland benchmark was used to set this benchmark (Note 22)?

Bearings and distances are now shown but the information is not clear with all the over writes.  A clear separate roadway survey plan for acceptance will be required.

- A letter which shows Windsor Construction’s financial capacity has been provided.  However, the relationship between Windsor Construction and the owner is unclear.  Please provide evidence that Windsor Construction plans to finance the project on behalf of the applicant.

Note that the Planning Authority may request additional information during the continued review of the proposal according to applicable laws, ordinances and regulations.

Single Family House, Additional Comments

Environmental

Please see notes above.

Zoning

Your most recent submittal includes a written description of the outsale lot.  Ann Machado, Zoning Administrator, notes that a copy of the recorded deed for the sale of this lot will be required before issuance of a certificate of occupancy for the single family home.

Ann Machado also writes of the site plan,

Two of the three porches are now shown but the 8' x 47' porch on the "front" of the house, north side, facing Bancroft Street is not shown on the site plan.

Again, note that the Planning Authority may request additional information during the continued review of the proposal according to applicable laws, ordinances and regulations.

Planning Staff Recommendation

Based upon the staff review above, I recommend that the applicant proceed by submitting one (1) complete paper set of revised plans, along with documentation, to address staff comments.  Upon receipt of the revised material, the City of Portland will review the additional plans and information for conformance with applicable ordinances.    Please be aware that an application expires within 120 days of the date upon which this written request for additional information was made.

As before, if you have any questions or feel that a meeting would be helpful in formulating your revised plans, feel free to contact me at 874-8723 or by email at hcd@portlandmaine.gov.

Sincerely,

Nell Donaldson

Planner

# Attachments:

# Memo from David Margolis-Pineo, Department of Public Services, dated 9/19/12

# Memo from David Senus, PE, Woodard and Curran, dated 9/20/12

# Email from Ann Machado, Zoning Adminstrator, dated 9/26/12

# Electronic Distribution:

Alexander Jaegerman, Planning Division Director

Barbara Barhydt, Development Review Services Manager

Danielle West-Chuhta, Associate Corporation Counsel

Marge Schmuckal, Zoning Administrator

Katherine Earley, City Engineer, Public Services

David Margolis-Pineo, Deputy City Engineer

Captain Chris Pirone, Fire

Jeff Tarling, City Arborist

Tom Errico, P.E.,  TY Lin Associates

David Senus, P.E.,  Woodard & Curran