Structural Statement of Special Inspections

| Project: | Thompson Point Depot |
| --- | --- |
| Location: | Thompson Point |
| Owner: |  |
| This Statement of Special Inspections encompass the following discipline: Structural |

This Statement of Special Inspections is submitted as a condition for permit issuance in accordance with the Special Inspection and Structural Testing requirements of the Building Code.  It includes a schedule of Special Inspection services applicable to this project as well as the name of the Structural Special Inspection Coordinator (SSIC) and the identity of other approved agencies to be retained for conducting these inspections and tests.

The Structural Special Inspection Coordinator shall keep records of all Structural inspections and shall furnish inspection reports to the Building Code Official (BCO) and the Structural Registered Design Professional in Responsible Charge (SRDP).  Discovered discrepancies shall be brought to the immediate attention of the Contractor for correction.  If such discrepancies are not corrected, the discrepancies shall be brought to the attention of the Building Official and the Structural Registered Design Professional in Responsible Charge.  The Special Inspection program does not relieve the Contractor of his or her responsibilities.

Interim reports shall be submitted to the Building Official and the Structural Registered Design Professional in Responsible Charge at an interval determined by the SSIC and the BCO.

A Final Report of Special Inspections documenting completion of all required Special Inspections, testing and correction of any discrepancies noted in the inspections shall be submitted to the BCO prior to issuance of a Certificate of Use and Occupancy.

Job site safety and means and methods of construction are solely the responsibility of the Contractor.

| Interim Report Frequency: | Upon request of Building Official ________ | or per attached schedule. |
| --- | --- | --- |
| Prepared by: |  | Design Professional Seal |
| Aaron C. Jones, P.E. |  |  |
| (type or print name of the Structural Registered Design Professional in Responsible Charge) |  |  |
|  | 5/22/2014 |  |  |
| Signature | Date |  |  |

| Owner’s Authorization: |  | Building Code Official’s Acceptance: |
| --- | --- | --- |
| Signature | Date |  | Signature | Date |

Structural Statement of Special Inspections (Continued)

## List of Agents

| Project: | Thompson Point Depot |
| --- | --- |
| Location: | Thompson Point |
| Owner: | Redfern LWS |
| This Statement of Special Inspections encompass the following discipline: Structural |

(Note: Statement of Special Inspections for other disciplines may be included under a separate cover)

This Statement of Special Inspections / Quality Assurance Plan includes the following building systems:

Soils and Foundations

Cast-in-Place Concrete

Precast Concrete System

Masonry Systems

Structural Steel

Wood Construction		 		   Special Cases

| Special Inspection Agencies | Firm | Address, Telephone, e-mail |
| --- | --- | --- |
| 1. STRUCTURAL Special Inspections Coordinator (SSIC) | Structural Integrity Consulting Engineers Inc | 77 Oak St. Portland, Maine 207-774-4614 Aaron@structuralinteg.com |
| 2. Special Inspector (SI 1) | TBD | TBD |
| 3. Special Inspector (SI 2) | TBD | TBD |
| 4. Testing Agency (TA 1) | TBD | TBD |
| 5. Testing Agency (TA 2) | TBD | TBD |
| 6. Other (O1) | TBD | TBD |

Note:  The inspectors and testing agencies shall be engaged by the Owner or the Owner’s Agent, and not by the Contractor or Subcontractor whose work is to be inspected or tested. Any conflict of interest must be disclosed to the Building Official, prior to commencing work.

Structural Statement of Special Inspections (Continued)

Final Report of Special Inspections (SSIC/SI 1)

[To be completed by the Structural Special Inspections Coordinator (SSIC/SI 1).  Note that all Agent’s Final Reports must be received prior to issuance.]

| Project: | Thompson Point Depot |
| --- | --- |
| Location: | Thompson Point |
| Owner: |  |
| Owner’s Address: |  |
| Architect of Record: | Bill Hopkins | Archetype |
|  | (name) | (firm) |
| Structural Registered Design Professional in Responsible Charge: |  |
|  | Aaron C. Jones | Structural Integrity Consulting Eng. |
|  | (name) | (firm) |

To the best of my information, knowledge and belief, the Special Inspections required for this project, and itemized in the Statement of Special Inspections submitted for permit, have been performed and all discovered discrepancies have been reported and resolved.

Interim reports submitted prior to this final report form a basis for and are to be considered an integral part of this final report.

| Respectfully submitted, |  |  |  |
| --- | --- | --- | --- |
| Structural Special Inspection Coordinator |  |  |  |
| (Type or print name) |  |  |  |
| (Firm Name) |  |  |  |
| Signature | Date |  | Licensed Professional Seal |

Structural Schedule of Special Inspections

##### Qualifications of Inspectors and Testing Technicians

The qualifications of all personnel performing Special Inspection and testing activities are subject to the approval of the Building Official. The credentials of all Inspectors and testing technicians shall be provided to the Special Inspector for their records.  NOTE VERIFICATION THAT QUALIFIED INDIVIDUALS ARE AVAILABLE TO PERFORM STIPULATED TESTING AND/OR INSPECTION SHOULD BE PROVIDED PRIOR TO SUBMITTING STATEMENT.  AGENT QUALIFICATIONS IN SCHEDULE ARE SUGGESTIONS ONLY; FINAL QUALIFICATIONS ARE SUBJECT TO THE DISCRETION OF THE REGISTERED DESIGN PROFESSIONAL PREPARING THE SCHEDULE.

Key for Minimum Qualifications of Inspection Agents:

When the Registered Design Professional in Responsible Charge or Special Inspector of Record deems it appropriate that the individual performing a stipulated test or inspection have a specific certification, license or experience as indicated below, such requirement shall be listed below and shall be clearly identified within the schedule under the Agent Qualification Designation.

###### PE/SE		Structural Engineer – a licensed SE or PE specializing in the design of building structures

PE/GE		Geotechnical Engineer – a licensed PE specializing in soil mechanics and foundations

EIT	Engineer-In-Training – a graduate engineer who has passed the Fundamentals of Engineering examination

Experienced Testing Technician

ETT	Experienced Testing Technician – An Experienced Testing Technician with a minimum 5 years experience with the stipulated test or inspection

American Concrete Institute (ACI) Certification

ACI-CFTT	Concrete Field Testing Technician – Grade 1

ACI-CCI		Concrete Construction Inspector

ACI-LTT		Laboratory Testing Technician – Grade 1&2

ACI-STT		Strength Testing Technician

American Welding Society (AWS) Certification

AWS-CWI	Certified Welding Inspector

AWS/AISC-SSI	Certified Structural Steel Inspector

American Society of Non-Destructive Testing (ASNT) Certification

ASNT		Non-Destructive Testing Technician – Level II or III.

International Code Council (ICC) Certification

ICC-SMSI	Structural Masonry Special Inspector

ICC-SWSI	Structural Steel and Welding Special Inspector

ICC-SFSI	Spray-Applied Fireproofing Special Inspector

ICC-PCSI	Prestressed Concrete Special Inspector

ICC-RCSI	Reinforced Concrete Special Inspector

National Institute for Certification in Engineering Technologies (NICET)

NICET-CT	Concrete Technician – Levels I, II, III & IV

NICET-ST	Soils Technician - Levels I, II, III & IV

NICET-GET	Geotechnical Engineering Technician - Levels I, II, III & IV

Other

Structural Schedule of Special Inspections

SOILS & FOUNDATION CONSTRUCTION

| VERIFICATION AND INSPECTION IBC Section 1704.7, 1704.8, 1704.9 | Y/N | EXTENT: CONTINUOUS, PERIODIC, SUBMITTAL, OR NONE | COMMENTS | AGENT | AGENT QUALIFICATION | TASK COMPLETED |
| --- | --- | --- | --- | --- | --- | --- |
| 1. Verify existing soil conditions, fill placement and load bearing requirements |  |  |  |  |  |  |
| a. Prior to placement of prepared fill, determine that the site has been prepared in accordance with the approved soils report. | Y | P | IBC 1704.7.1 |  | PE/GE, EIT or ETT |  |
| b. During placement and compaction of fill material, verify material being used and maximum lift thickness comply with the approved soils report. | Y | P | IBC 1704.7.2 |  | PE/GE, EIT or ETT |  |
| c. Test in-place dry density of compacted fill complies with the approved soils report. | Y | p | IBC 1704.7.2 |  | PE/GE, EIT or ETT |  |

Structural Schedule of Special Inspections

CONCRETE CONSTRUCTION

| VERIFICATION AND INSPECTION IBC Section 1704.4 | Y/N | EXTENT: CONTINUOUS, PERIODIC, SUBMITTAL, OR NONE | COMMENTS | AGENT | AGENT QUALIFICATION | TASK COMPLETED |
| --- | --- | --- | --- | --- | --- | --- |
| 1. Inspection of reinforcing steel and placement | Y | P | ACI 318: 3.5, 7.1-7.7 |  | PE/SE or EIT |  |
| 3. Inspect bolts to be installed in concrete prior to and during placement of concrete where allowable loads have been increased | N | C | IBC 1912.5 |  | PE/SE or EIT |  |
| 4. Verifying use of required design mix | Y | P | ACI 318: Ch 4, 5.2-5.4 |  | PE/SE or EIT |  |
| 5. At time fresh concrete is sampled to fabricate specimens for strength test, perform slump and air content test and temperature | Y | C | ASTM C 172 ASTM C 31 ACI 318: 5.6, 5.8 |  | ACI-CFTT or ACI-STT |  |
| 6. Inspection of concrete and shotcrete placement for proper application techniques | Y | C | ACI 318: 5.9, 5.10 |  | PE/SE or EIT |  |
| 7. Inspection for maintenance of specified curing temperature and techniques | Y | P | ACI 318: 5.11-5.13 |  | PE/SE or EIT |  |

Structural Schedule of Special Inspections - STEEL CONSTRUCTION

| VERIFICATION AND INSPECTION IBC Section 1704.3 | Y/N | EXTENT: CONTINUOUS, PERIODIC, SUBMITTAL, OR NONE | COMMENTS | AGENT | AGENT QUALIFICATION | TASK COMPLETED |
| --- | --- | --- | --- | --- | --- | --- |
| 1. Material verification of high-strength bolts, nuts and washers: |  |  |  |  |  |  |
| a. Identification markings to conform to ASTM standards specified in the approved construction documents. | Y | S | Applicable ASTM material specifications; AISC 335, Section A3.4; AISC LRFD, Section A3.3 |  | PE/SE or EIT |  |
| b. Manufacturer's certificate of compliance required. | Y | S |  |  | PE/SE or EIT |  |
| 2. Inspection of high-strength bolting |  |  |  |  |  |  |
| a. Bearing-type connections. | N | P | AISC LRFD Section M2.5 IBC Sect 1704.3.3 |  | AWS/AISC-SSI |  |
| 3. Material verification of structural steel (IBC Sect 1708.4): |  |  |  |  |  |  |
| a. Identification markings to conform to ASTM standards specified in the approved construction documents. | Y | S | ASTM A 6 or ASTM A 568 IBC Sect 1708.4 |  | PE/SE or EIT |  |
| b. Manufacturers' certified mill test reports. | Y | S | ASTM A 6 or ASTM A 568 IBC Sect 1708.4 |  | PE/SE or EIT |  |
| 4. Material verification of weld filler materials: |  |  |  |  |  |  |
| a. Identification markings to conform to AWS specification in the approved construction documents. | Y | S | AISC, ASD, Section A3.6; AISC LRFD, Section A3.5 |  | PE/SE or EIT |  |
| b. Manufacturer's certificate of compliance required. | Y | S |  |  | PE/SE or EIT |  |
| 5. Submit current AWS D1.1 welder certificate for all field welders who will be welding on this project. | Y | S | AWS D1.1 |  | PE/SE or EIT |  |
| 6. Inspection of welding (IBC 1704.3.1): |  |  |  |  |  |  |
| a. Structural steel: |  |  |  |  |  |  |
| 4) Single-pass fillet welds< 5/16” | Y | P |  |  | AWS-CWI |  |
| 5) Floor and deck welds. | Y | P | AWS D1.3 |  | AWS-CWI |  |
| b. Reinforcing steel (IBC Sect 1903.5.2): |  |  |  |  |  |  |
| 3) Shear reinforcement. | Y | C | AWS D1.4 ACI 318: 3.5.2 |  | AWS-CWI |  |
| 7. Inspection of steel frame joint details for compliance (IBC Sect 1704.3.2) with approved construction documents: |  |  |  |  |  |  |
| a. Details such as bracing and stiffening. | Y | P |  |  | PE/SE or EIT |  |
| b. Member locations. | Y | P |  |  | PE/SE or EIT |  |
| c. Application of joint details at each connection. | Y | P |  |  | PE/SE or EIT |  |

Structural Schedule of Special Inspection Services

FABRICATION AND IMPLEMENTATION PROCEDURES – STRUCTURAL STEEL

| VERIFICATION AND INSPECTION IBC Section 1704.2 | Y/N | EXTENT: CONTINUOUS, PERIODIC, SUBMITTAL, OR NONE | COMMENTS | AGENT | AGENT QUALIFICATION | TASK COMPLETED |
| --- | --- | --- | --- | --- | --- | --- |
| 1. Fabrications Procedures: Review of fabricator’s written procedural and quality control manuals and periodic auditing of fabrication practices by an approved special inspection agency. At the completion of fabrication, the approved fabricator shall submit a certificate of compliance to the building code official stating that the work was performed in accordance with the approved construction documents. -OR- | Y | S | Fabricator shall submit one of the two qualifications |  | PE/SE or EIT |  |
| 2. AISC Certification |  |  |  |  |  |  |
| 3. At completion of fabrication, the approved fabricator shall submit a certificate of compliance to the building code official stating that the work was performed in accordance with the approved construction documents. | Y | S | IBC 1704.2.2 |  | PE/SE or EIT |  |

Contractor’s Statement of Responsibility

Each contractor responsible for the construction or fabrication of a system or component designated in the Quality Assurance Plan must submit a Statement of Responsibility.   The Statement of Responsibility is required for Seismic Design Category C or higher. Make additional copies of this form as required.

Project: Thompson Point Depot

Contractor’s Name:Portland Builders

Address:

License No.:

Description of designated building systems and components included in the Statement of Responsibility:

Contractor’s Acknowledgment of Special Requirements

I hereby acknowledge that I have received, read, and understand the Quality Assurance Plan and Special Inspection program.

I hereby acknowledge that control will be exercised to obtain conformance with the construction documents approved by the Building Official.

________________________________          _______________

Signature                                                           Date

Contractor’s Provisions for Quality Control

Procedures for exercising control within the contractor’s organization, the method and frequency of reporting and the distribution of reports is attached to this Statement.

Identification and qualifications of the person(s) exercising such control and their position(s) in the organization are attached to this Statement.

Quality Assurance Plan – Seismic and Wind

QUALITY ASSURANCE FOR SEISMIC RESISTANCE CHECK LIST [IBC 1705]

| Seismic Design Category | B |
| --- | --- |

| For Seismic Design Category C or higher: |
| --- |
| Structural: |
|  | The seismic-force-resisting systems |
|  | Steel Braced Frames and associated connections/anchorage |
|  | Steel Moment Frames and associated connections |
|  | Shear walls: CMU Wood Concrete | Diaphragms: Floor Roof |
|  | Other: |  |

QUALITY ASSURANCE FOR WIND RESISTANCE CHECK LIST [IBC 1706]

| Wind Exposure Category | C |
| --- | --- |

| REQUIRED | NOT REQUIRED | NOT APPLICABLE | QUALITY ASSURANCE PLAN REQUIREMENTS (A Quality Assurance Plan is required where indicated below) |
| --- | --- | --- | --- |
|  |  |  | In wind exposure Categories A and B, where the 3-second-gust basic wind speed is 120 miles per hour (mph) (52.8 m/sec) or greater. |
|  |  |  | In wind exposure Categories C and D, where the 3-second-gust basic wind speed is 110 mph (49 m/sec) or greater. |