From: 	"Errico, Thomas A" <TERRICO@wilbursmith.com>

To:	"Molly Casto" <MPC@portlandmaine.gov>

Date: 	8/12/2008 3:20:17 PM

Subject: 	Burger King -- Riverside Street

Molly -

A status report on my prior comments is noted below according to plans

prepared by Gorrill-Palmer Consulting Engineers, Inc.

1.	The entrance on Riverside Street should be restricted to

right-turn entry and exit movements only.  I would also recommend that a

median island be provided in Riverside Street to physically prevent

left-turn movements.  This island will also be compatible with the

restricted driveway on the opposite side of Riverside Street.  These

improvements will need to be compatible with future PACTS improvements.

Status:  The plans have been prepared to prevent left-turn movements

from the site only.  I concur with this restriction and have no further

comment.

2.	I need to confirm with Jim Carmody on the need for crosswalks at

the driveway entrances.

Status:  The plans are acceptable and I have no further comment.

3.	The northerly radius on Riverside Street should be ADA

compliant.

Status:  The plans have been revised and I have no further comment.

4.	The drive-through lane does not provide a "bail-out" option.

This condition seems atypical for a drive-through restaurant.

Status:  This issue was discussed with the applicant and I find the

proposed condition to be acceptable.

5.	The parking stalls are 20 feet long.  The parking layout should

be revised to 9' x 19' parking stall sizes, the City standard.

Status:  The plans have been revised and I have no further comment.

6.	The parking aisle is proposed to be 25 feet.  The aisle width

should be 24 feet, the City standard.

Status:  I support a waiver for the aisle to be 1 foot wider than the

City standard.  I have no further comment.

7.	The radii on Larabee Road should be granite and be ADA

compliant.

Status:  The radii should be granite and a sidewalk should be extended

to the opposite side of the driveway (with an ADA compliant ramp)

towards the City of Westbrook boundary.

8.	The applicant should provide a turning template for vehicle

maneuvers onto Larabee Road and assess whether the existing island needs

modifications.

Status:  I reviewed the provided material and have no further comment.

9.	The applicant should provide information on how truck deliveries

will occur and access/egress movements for trucks.

Status:  I have no further comment.

10.	The applicant should provide pedestrian accommodations from

Larabee Road to the restaurant.

Status:  Outstanding

11.	A cross parcel connection between the proposed site and the

rear/northerly site should be maintained.

Status:  A connection is provided on the north east portion of the site

which I find acceptable.

12.	The applicant should provide a summary of traffic generating

increases/decreases for the Saturday peak hour.

Status:  Information has been provided and I have no further comment.

If you have any questions, please contact me.

Best regards,

Thomas A. Errico, P.E.

Senior Transportation Engineer

Wilbur Smith Associates

59 Middle Street

Portland, Maine 04101

w: 207.871.1785 f: 207.871.5825

TErrico@WilburSmith.com

www.WilburSmith.com <http://www.wilbursmith.com/>

CC:	"James Carmody" <JPC@portlandmaine.gov>, "Katherine Earley" <KAS@portlandmaine.gov>