From: 	"Errico, Thomas A" <TERRICO@wilbursmith.com>

To:	"Molly Casto" <MPC@portlandmaine.gov>

Date: 	Tue, May 27, 2008  1:57 PM

Subject: 	Burger King - 132 Riverside Street

Molly -

The following summarizes my initial comments following my review of

materials contained in the April 30, 2008 Minor Development Site Plan

Application prepared by Gorrill-Palmer Consulting Engineers, Inc.

1.	The entrance on Riverside Street should be restricted to

right-turn entry and exit movements only.  I would also recommend that a

median island be provided in Riverside Street to physically prevent

left-turn movements.  This island will also be compatible with the

restricted driveway on the opposite side of Riverside Street.  These

improvements will need to be compatible with future PACTS improvements.

2.	I need to confirm with Jim Carmody on the need for crosswalks at

the driveway entrances.

3.	The northerly radius on Riverside Street should be ADA

compliant.

4.	The drive-through lane does not provide a "bail-out" option.

This condition seems atypical for a drive-through restaurant.

5.	The parking stalls are 20 feet long.  The parking layout should

be revised to 9' x 19' parking stall sizes, the City standard.

6.	The parking aisle is proposed to be 25 feet.  The aisle width

should be 24 feet, the City standard.

7.	The radii on Larabee Road should be granite and be ADA

compliant.

8.	The applicant should provide a turning template for vehicle

maneuvers onto Larabee Road and assess whether the existing island needs

modifications.

9.	The applicant should provide information on how truck deliveries

will occur and access/egress movements for trucks.

10.	The applicant should provide pedestrian accommodations from

Larabee Road to the restaurant.

11.	A cross parcel connection between the proposed site and the

rear/northerly site should be maintained.

12.	The applicant should provide a summary of traffic generating

increases/decreases for the Saturday peak hour.

I want to emphasize that these are my initial comments and additional

input is likely.  If you have any questions, please contact me.

Best regards,

Thomas A. Errico, P.E.

Senior Transportation Engineer

Wilbur Smith Associates

59 Middle Street

Portland, Maine 04101

w: 207.871.1785 f: 207.871.5825

TErrico@WilburSmith.com

www.WilburSmith.com <http://www.wilbursmith.com/>

CC:	"James Carmody" <JPC@portlandmaine.gov>, "Katherine Earley" <KAS@portlandmaine.gov>