Site Plan Review Notes: Burger King. 132 Riverside Street

Scope of Review: Minor Site Plan

Existing: convenience store/gas station with 8 fueling stations and a restaurant with drive-thru (Tim Hortons)

Owner: Weber Energy Fuels

Applicant: Mastoran Corporation *Check deeds

Zone: B-4

Parcel- .77 aces

Proposed:

- 2,200 sf Burger King fast food restaurant with drive-thru.

- 2 driveways (one on Riverside/one on Larabee)

  - Both driveways are proposed 2-way. (see traffic comments)

- Both curb cuts are existing

- Seating for 62 people

- 31 Parking Spaces

- Space for 10 cars –stacking

- 26 x 13 trash enclosure.

Comments: - planner review

Need bike racks. None proposed

2 bike spaces for every 10 car spaces required = 6 spaces required.  (Section 14-526 (2) (c))

Existing Exxon sign on concrete base- proposed to remain.  (?)- Just the base? Check on this one.

Parking spaces encroaching on rear and side yard setbacks.  Check the ordinance on this -  Do the setbacks just apply to structures?

2 menu boards (one considered “optional”- what does this mean?): does the second menu board have an intercom?  Make sure they know the rules if there are sound requirements and that it can’t play a prerecorded message, etc.  They will need to submit sound info on the mechanicals.

Vertical or sloped granite curbing proposed in various areas:  not continuous.  Look at Moody’s as an example.  Should they curb all the parking spaces?  Some don’t have any curb stops.  Jeff would like to see bituminous cape cod berm along the northern side to protect landscaping.  Perhaps they should enclose the entire site?  At least provide curb stops at parking spaces.

Construction entrance proposed along Riverside Street

Stormwater- outlet into existing drainage swale at south end of parcel.

Parking spaces- proposed at 9’ x 20.  Exceed minimum size requirements of City tech standards.

Existing easements: Oil pipeline.  Check into this.  Did they provide details?  If so make sure there aren’t any restrictions that we neeed to be aware of.

Neighbor’s encroachment and existing easement.  We need to work this out to be sure there aren’t conflicts. Neighbor = John Locke.  I called him and left a message on 5/14/08.

Sidewalk- adding 5’ wide bituminous sidewalk along riverside entrance driveway with tip downs.  Check materials policy.

2 rectangular areas defined on the plans (north side of proposed building – what are these?  Need more information from applicant.