Structural Statement of Special Inspections

Project:	Building Addition – Portland Sports Complex

Location:	512 Warren Avenue, Portland, Maine

Owner: 	Portland Sports Complex – Jim Gratello

This Statement of Special Inspections encompass the following discipline: Structural – Foundations

This Statement of Special Inspections is submitted as a condition for permit issuance in accordance with the Special Inspection and Structural Testing requirements of the Building Code.  It includes a schedule of Special Inspection services applicable to this project as well as the name of the Structural Special Inspection Coordinator (SSIC) and the identity of other approved agencies to be retained for conducting these inspections and tests.

The Structural Special Inspection Coordinator shall keep records of all Structural inspections and  shall furnish inspection  reports  to  the  Building  Code  Official  (BCO)  and  the  Structural  Registered  Design  Professional  in Responsible Charge (SRDP).  Discovered discrepancies shall be brought to the immediate attention of the Contractor for correction.   If such discrepancies are not corrected, the  discrepancies shall be brought to the attention of the Building Official and the Structural Registered Design Professional in Responsible Charge.  The Special Inspection program does not relieve the Contractor of his or her responsibilities.

Interim reports shall be submitted to the Building Official and the Structural Registered Design  Professional in

Responsible Charge at an interval determined by the SSIC and the BCO.

A  Final Report of Special Inspections documenting completion of all required Special Inspections,  testing and correction of any discrepancies noted in the inspections shall be submitted to the BCO  prior to issuance of a Certificate of Use and Occupancy.

Job site safety and means and methods of construction are solely the responsibility of the Contractor.

Interim Report Frequency:	Upon request of Building Official

or	per attached schedule.

Prepared by:

Ted Greenlaw, P.E.

(Structural Registered Design Professional in Responsible Charge)

Signature	Date

Design Professional Seal

Owner’s Authorization:	Building Code Official’s Acceptance:

Signature	Date	Signature	Date

Structural Statement of Special Inspections (Continued)

List of Agents

Project:	Building Addition – Portland Sports Complex

Location:	512 Warren Avenue, Portland, Maine

Owner:	Portland Sports Complex – Jim Gratello

This Statement of Special Inspections encompass the following discipline: Structural - Foundations

(Note: Statement of Special Inspections for other disciplines may be included under a separate cover)

This Statement of Special Inspections / Quality Assurance Plan includes the following building systems:

Soils and Foundations Cast-in-Place Concrete Precast Concrete System Masonry Systems Structural Steel

Wood Construction	Special Cases

| Special Inspection Agencies | Firm | Address, Telephone, e-mail |
| --- | --- | --- |
| 1. STRUCTURAL Special Inspections Coordinator (SSIC) |  |  |
| 2. Special Inspector (SI 1) | Ted Greenlaw, P.E. | 183 Columbia Road Hanover, MA 02339 (781)- 826-8369 |
| 3. Special Inspector (SI 2) | John Turner Consulting, Inc. | 73 Rainmaker Drive Portland, ME (207) 883-7878 |
| 4. Testing Agency (TA 1) | John Turner Consulting, Inc. | 73 Rainmaker Drive Portland, ME (207) 883-7878 |
| 5. |  |  |
| 6. |  |  |

Note:  The inspectors and testing agencies shall be engaged by the Owner or the Owner’s Agent, and not by the Contractor or Subcontractor whose work is to be inspected or tested. Any conflict of interest must be disclosed to the Building Official, prior to commencing work.

Structural Statement of Special Inspections (Continued)

Final Report of Special Inspections (SSIC/SI 1)

[To be completed by the Structural Special Inspections Coordinator (SSIC/SI 1). Note that all Agent’s Final Reports must be received prior to issuance.]

Project:  Building Addition – Portland Sports Complex

Location:  512 Warren Avenue, Portland, Maine

Owner:  Portland Sports Complex – Jim Gratello

Owner’s Address: 512 Warren Avenue, Portland, Maine

Architect of Record:	N/A

Structural Registered Design Professional in Responsible Charge:	Ted Greenlaw, P.E.

To the best of my information, knowledge and belief, the Special Inspections required for this project, and itemized in the Statement of Special Inspections submitted for permit, have been performed and all discovered discrepancies have been reported and resolved.

Interim reports submitted prior to this final report form a basis for and are to be considered an integral part of this final report.

Respectfully submitted,

Structural Special Inspection Coordinator

(Type or print name)

(Firm Name)

Signature	Date

Licensed Professional Seal

Project: New Building for Phoenix Property Management

Date Prepared: December 8, 2011

Structural Statement of Special Inspections (Continued)

Special Inspector’s/Agent’s Final Report

Project:	Building Addition – Portland Sports Complex

Special Inspector or Agent:

Designation:

To the best of my information, knowledge and belief, the Special Inspections or testing required for this project, and designated  for  this  Inspector/Agent  in  the  Statement  of  Special  Inspections  submitted  for  permit,  have  been performed and all discovered discrepancies have been reported and resolved.

Interim reports submitted prior to this final report form a basis for and are to be considered an integral part of this final report.

Respectfully submitted, Special Inspector or Agent:

(Type or print name)

Signature	Date

Licensed Professional Seal or

Certification Number

Project: New Building for Phoenix Property Management

Date Prepared: December 8, 2011

Structural Schedule of Special Inspections

Qualifications of Inspectors and Testing Technicians

The qualifications of all personnel performing Special Inspection and testing activities are subject to the approval of the Building Official. The credentials of all Inspectors and testing technicians shall be provided to the Special Inspector for their records.	NOTE VERIFICATION THAT QUALIFIED INDIVIDUALS ARE AVAILABLE TO PERFORM STIPULATED TESTING AND/OR INSPECTION SHOULD BE PROVIDED PRIOR TO SUBMITTING STATEMENT.  AGENT QUALIFICATIONS IN SCHEDULE ARE SUGGESTIONS ONLY; FINAL QUALIFICATIONS ARE  SUBJECT  TO  THE  DISCRETION  OF  THE  REGISTERED  DESIGN  PROFESSIONAL  PREPARING  THE SCHEDULE.

Key for Minimum Qualifications of Inspection Agents:

When  the  Registered  Design  Professional  in  Responsible  Charge  or  Special  Inspector  of  Record  deems  it appropriate that the individual performing a stipulated test or inspection have a  specific certification, license or experience as indicated below, such requirement shall be listed  below  and shall be clearly identified within the schedule under the Agent Qualification Designation.

PE/SE	Structural Engineer – a licensed SE or PE specializing in the design of building structures

PE/GE	Geotechnical Engineer – a licensed PE specializing in soil mechanics and foundations

EIT	Engineer-In-Training – a graduate engineer who has passed the Fundamentals of Engineering examination

Experienced Testing Technician

ETT	Experienced Testing Technician – An Experienced Testing Technician with a minimum 5 years experience with the stipulated test or inspection

American Concrete Institute (ACI) Certification

ACI-CFTT	Concrete Field Testing Technician – Grade 1

ACI-CCI	Concrete Construction Inspector

ACI-LTT	Laboratory Testing Technician – Grade 1&2

ACI-STT	Strength Testing Technician

American Welding Society (AWS) Certification

AWS-CWI	Certified Welding Inspector

AWS/AISC-SSI	Certified Structural Steel Inspector

American Society of Non-Destructive Testing (ASNT) Certification ASNT	Non-Destructive Testing Technician – Level II or III. International Code Council (ICC) Certification

ICC-SMSI	Structural Masonry Special Inspector

ICC-SWSI	Structural Steel and Welding Special Inspector ICC-SFSI	Spray-Applied Fireproofing Special Inspector ICC-PCSI	Prestressed Concrete Special Inspector

ICC-RCSI	Reinforced Concrete Special Inspector

National Institute for Certification in Engineering Technologies (NICET)

NICET-CT	Concrete Technician – Levels I, II, III & IV NICET-ST	Soils Technician - Levels I, II, III & IV

NICET-GET	Geotechnical Engineering Technician - Levels I, II, III & IV

Other

Structural Schedule of Special Inspections

SOILS & FOUNDATION CONSTRUCTION

| VERIFICATION AND INSPECTION IBC Section 1704.7, 1704.8, 1704.9 | Y/N | EXTENT: CONTINUOUS, PERIODIC, SUBMITTAL, OR NONE | COMMENTS | AGENT | AGENT QUALIFICATION |
| --- | --- | --- | --- | --- | --- |
| Verify existing soil conditions, fill placement and load bearing requirements |  |  |  |  |  |
| 1. Verify materials below shallow foundations are adequate to achieve design bearing capacity | Y | P | IBC 1704.7 | SI2 | PE/GE, EIT or ETT |
| 2. Verify excavations are extended to proper depth and have reached proper material | Y | P | IBC 1704.7 | SI2 | PE/GE, EIT or ETT |
| 3. Perform classification and testing of compacted fill materials | Y | P | IBC 1704.7 | SI2 | PE/GE, EIT or ETT |
| 4. Verify use of proper materials, densities and lift thicknesses during placement and compaction of compacted fill | Y | C | IBC 1704.7 | SI2 | PE/GE, EIT or ETT |
| 5. Prior to placement of compacted fill, observe subgrade and verify that site has been prepared properly | Y | P | IBC 1704.7 | SI2 | PE/GE, EIT or ETT |

Structural Schedule of Special Inspections

CONCRETE CONSTRUCTION

| VERIFICATION AND INSPECTION IBC Section 1704.4 | Y/N | EXTENT: CONTINUOUS, PERIODIC, SUBMITTAL, OR NONE | COMMENTS | AGENT | AGENT QUALIFICATION |
| --- | --- | --- | --- | --- | --- |
| 1. Inspection of reinforcing steel, including prestressing tendons, and placement | Y | P | ACI 318: 3.5, 7.1-7.7 | SI1 | PE/SE, EIT or ICC- RCSI |
| 2. Inspection of reinforcing steel welding (Refer to Item 6B in Steel Construction Table below) | NA | P | AWS D1.4 ACI 318: 3.5.2 |  | AWS-CWI |
| 3. Inspect bolts to be installed in concrete prior to and during placement of concrete where allowable loads have been increased or where strength design is used | Y | C | IBC 1911.5, 1912.1 ACI 318: 8.1.3, 21.2.8 | SI1 | PE/SE, EIT or ICC- RCSI |
| 4. Inspection of anchors installed in hardened concrete | Y | P | IBC 1912.1 ACI 318: 3.8.6, 8.1.3, 21.2.8 | SI1 | PE/SE, EIT or ICC- RCSI |
| 5. Verifying use of required design mix | Y | P | ACI 318: Ch 4, 5.2-5.4 | SI1, SI2 or TA1 | PE/SE, EIT or ICC- RCSI |
| 6. At time fresh concrete is sampled to fabricate specimens for strength test, perform slump and air content test and temperature In the absence of project specific specifications, the frequency of testing shall be per the schedule following this table | Y | C | ASTM C 172 ASTM C 31 ACI 318: 5.6, 5.8 IBC 1913.10 | TA1 | ACI-CFTT or ACI-STT |
| 7. Inspection of concrete and shotcrete placement for proper application techniques | Y | C | ACI 318: 5.9, 5.10 | SI1, SI2 or TA1 | PE/SE, EIT or ICC- RCSI |
| 8. Inspection for maintenance of specified curing temperature and techniques | Y | P | ACI 318: 5.11- 5.13 | SI1, SI2 or TA1 | PE/SE, EIT or ICC- RCSI |

Concrete Testing Frequency:

Concrete cylinders shall be taken, and fresh concrete tested at least once per placement or at the following intervals:

1. Retaining walls and footings:	50 cubic yards

2. Isolated Footings:	25 cubic yards

3. Slabs:	50 cubic yards