1

| SECTION 2 - CONCRETE CONSTRUCTION (IBC 1704.4) |
| --- |
| CONCRETE MATERIALS | 2.1a | Review mix design. | Verify approval of all mixes intended for use. |  |  |  |  |
|  | 2.1b | Review reinforcement grade. | Inspect identifying marks on reinforcing steel. |  |  |  |  |
|  | 2.1c | Review submittals. | Verify acceptance of propriety products and reinforcing steel shop drawings. Review requirements of reinforcing steel on placement drawings. |  |  |  |  |
| REINFORCING STEEL | 2.2a | Inspect condition and placement of reinforcing steel. | All reinforcing steel at walls, spread footings, columns and beams and column piers. Check prior to each concrete placement. |  |  |  |  |
| FORMWORK | 2.3a | Verify acceptability of substrate. | Prior to each concrete placement. |  |  |  |  |
|  | 2.3b | Verify dimensions and materials acceptability. | Prior to each concrete placement. |  |  |  |  |
| EMBEDMENTS | 2.4a | Inspect installation of anchor bolts, masonry dowels and other embedded items. | Inspect for each concrete placement. |  |  |  |  |
| CONCRETE OPERATIONS | 2.5a | Field testing of concrete slump, temperature, and air content. | All concrete placements. |  |  |  |  |
|  | 2.5b | Take concrete cylinder samples and perform compressive strength test. | All concrete placements. |  |  |  |  |
|  | 2.5c | Observe concrete placement. | Inspect placement procedures at all concrete placements. |  |  |  |  |
|  | 2.5d | Observe concrete curing technique and temperature. | Once daily when air temperature is above 32(F. Twice daily when temperature is below 32(F. |  |  |  |  |

| SECTION 3 - MASONRY CONSTRUCTION (IBC 1704.5) |
| --- |
| MATERIALS | 3.1a | Review material certification. | Verify that product certificates for all concrete masonry components, grout, mortar, reinforcing and embedded items have been approved. |  |  |  |  |
|  | 3.1b | Review grout materials and mix design. | Verify approval. |  |  |  |  |
|  | 3.1c | Review mortar materials and mix designs. | Verify approval of mortar for use in reinforced masonry. |  |  |  |  |
|  | 3.1d | Review strength determination in accordance with the Prism Strength method in ACI 530. | As directed by SER or Code Enforcement Officer. See contract documents for requirements. |  |  |  |  |
|  | 3.1e | Review of submittals. | Verify approval of reinforcing steel shop drawings and all items intended for use. |  |  |  |  |
|  | 3.1f | Preconstruction testing of grout. | Verify submittal approval. |  |  |  |  |
|  | 3.1g | Preconstruction testing of mortar. | Verify submittal approval. |  |  |  |  |
|  | 3.1h | Preconstruction Prism tests. | Verify submittal approval. |  |  |  |  |

| GENERAL MASONRY WORK | 3.2a | Inspect mortar mix proportions, mixing and placing procedures in reinforced masonry construction. | Inspect daily. |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | 3.2b | Inspect grout mixture proportions, mixing and placing procedures. | Inspect daily. |  |  |  |  |
|  | 3.2c | Inspect installation of horizontal, vertical and joint reinforcing including location, size, splices and positioning devices. | Inspect daily. |  |  |  |  |
|  | 3.2d | Inspect installation of anchorage devices and veneer ties. | Inspect daily. |  |  |  |  |
|  | 3.2e | Inspect installation of deformed bar reinforcement. | Inspect prior to each grout placement. |  |  |  |  |
|  | 3.2f | Field testing of grout, masonry prisms, and mortar utilized in reinforced masonry construction. | One test per 5000 square feet of reinforced masonry wall construction. |  |  |  |  |
| SECTION 4 - WOOD CONSTRUCTION (IBC 1704.6) |
| WOOD TRUSS FABRICATION | 4.1a | Review Fabricator QA/QC procedures manual. | One shop inspection required. |  |  |  |  |
| NOTE: SER may waive Fabricator shop inspection if Fabricator is currently | 4.1b | Review Fabricator QA/QC procedures implementation and conformance. | One shop inspection required. Visual inspection of shop conformance. |  |  |  |  |
| certified through the TPI Quality Certification Program | 4.1c | Review material certificates of compliance (wood grade and species, metal connectors). | Obtain copies of mill certificates for all lumber and metal connectors used in truss fabrication. |  |  |  |  |
|  | 4.1d | Inspect fabrication for conformance to approved shop drawings. Visually inspect grade stamps and metal plates. | Verify member sizes, piece marks and connection details match approved shop drawings. |  |  |  |  |
| WOOD TRUSS ERECTION | 4.2a | Inspect wood trusses and erection for conformance to approved shop drawings. | Verify all member sizes, piece marks and connection details. |  |  |  |  |
|  | 4.2b | Inspect wood truss bearing connection, bearing length, bridging, and bracing. Inspect installation of trusses for conformance to TPI HIB-91. | Visually inspect all trusses. |  |  |  |  |

|  | 4.2c | Inspect installation of metal connectors for compliance with contract documents and manufacturer=s recommendation. | Visually inspect all connections. |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| GENERAL WOOD CONSTRUCTION | 4.3a | Inspect installation, spacing and connection of wood framing for conformance to contract documents. | Visually inspect all framing and connections. |  |  |  |  |
|  | 4.3b | Inspect installation and fastening of structural wood panels to wood framing. |  |  |  |  |  |
|  | 4.3c | Inspect nail size and spacing at all diaphragms and shearwalls. | Visually inspect all. |  |  |  |  |
|  | 4.3d | Inspect installation of metal connectors for compliance with contract documents and manufacturer=s recommendation. | Visually inspect all connections. |  |  |  |  |
| SECTION 5 - PREPARED FILL (BOCA 1705.7) |
| PREPARED FILL SITE PREPARATION | 5.1a | Inspect site preparation and soil conditions prior to placement of fill. | Area of Concern: Fill placements beneath and adjacent to foundations. |  |  |  |  |
|  | 5.1b | Inspect filter fabric installation. | At Area of Concern, verify project and installation in accordance with contract documents. |  |  |  |  |
|  | 5.1c | Perform gradations and proctor tests. | Fill materials used at Area of Concern. |  |  |  |  |
|  | 5.1d | Inspector shall be present for all fill and compaction operations. | At Area of Concern. |  |  |  |  |
|  | 5.1e | Additional gradation and proctor tests. | At Area of Concern only at intervals of approximately 1500 cubic yards or whenever a change is detected. |  |  |  |  |
|  | 5.1f | Compaction tests. | Test each lift with a minimum of one test per 1000 square feet at Area of Concern. |  |  |  |  |
|  | 5.1g | Additional tests and retests. | Where compaction is found to be inadequate at Area of Concern. |  |  |  |  |
|  | 5.1h | Further tests. | Where previously approved areas have been disturbed at Area of Concern. |  |  |  |  |