Feb. 21, 2001

# To: Tony Vance

From:  Steve Wentworth,

Code Enforcement, Portland, Me.		874-8709

# Reference:   Lot #12, Copley Woods	(413-B-012)

- Stair stringers exceed 7 ¾” rise, actually measured at 1/16” over all steps

- Planes need to be amended to represent the cantilevered dormer change

- Data on floor girders needed & are but joints allowed?

- Are diagonal braces needed for interior of roof trusses?

- Data needed on laminated beams used @ dormers.

- 2nd. floor egress windows need to be remeasured.

- Pressure test on drain lines needed

- 1 1/4” rule for electrical conductors

- Framing not visible for skuttle to overhead.

- Kinked NMC to basement light fixture.

- No header at base of cellar stairs

- Floor girders not doubled as shown on plans adjacent to chimney

- Grounding conductor not clamped to ground rod.

Do Not Proceed with construction of this project until the above listed discrepancies are corrected.