22 August 2005

Mr. Stephen R. Bushey, P.E.,

DeLuca Hoffman Associates, Inc.,

778 Main Street, Suite 8,

South Portland, Maine 04106.

RE:   The Capacity to Handle an Anticipated Increase in Wastewater Flows,

From The Proposed Three Building Expansion, at the Roundhouse Site,

125 Presumpscot Street East, Portland, Maine.

Dear Mr. Bushey:

The existing eight inch diameter asbestos cement sanitary sewer pipe, located in Presumpscot Street East has adequate capacity to transport, while The Portland Water District sewage treatment facilities, located off Marginal Way, have adequate capacity to treat the anticipated wastewater flows of 795 GPD, from your proposed development.

Anticipated Wastewater Flows from the Proposed Expansion:

50 Proposed Office Employees @ 15 GPD/Employee				=  750 GPD

45 Proposed Additional Parking Spaces @ 1 GPD/Space				=    45 GPD

Total Proposed Increase in Wastewater Flows for this Project			=  795 GPD

The City combined sewer overflow (C.S.O.) abatement consent agreement, with the U.S.E.P.A. and the Maine D.E.P., requires C.S.O. abatement, as well as storm water mitigation, in order to offset any increase in sanitary flows, from all projects.

If The City can be of further assistance, please call 874-8832.

Sincerely,

CITY OF PORTLAND

Frank J Brancely, B.A., and M.A.

Senior Engineering Technician

FJB

cc:	Alexander Q. Jaegerman, Acting Co-Director, Department of Planning, and Urban Development, City of Portland

Kandice Talbot, Planner, Department of Planning, and Urban Development, City of Portland

Eric Labelle, P.E., City Engineer, City of Portland

Bradley A. Roland, P.E., Environmental Projects Engineer, City of Portland

Stephen K. Harris, Assistant Engineer, City of Portland

Jane Ward, Administrative Assistant, City of Portland

Desk file